## Slide 1: CATIA Machining Seminar
Originally created by Edwin Anderson
Updated by Cam Stefanic (Spring 2011)

## Slide 2: General Machining Terminology
NC - Numerically controlled
G Code - Coding language our CNC machines read
PO - Part Operation
MO - Machine Operation
Notes: Haas and Bridgeport Pics

## Slide 3: Two Schools of CNC Machining Thought
Solidworks
Solid Model
MasterCAM
NC Code
MasterCAM
Validation
HAAS
Machining
CATIA
Solid Model
NC Code
HAAS
Bridgeport

## Slide 4: University of Idaho Equipment
Mills
3-Axis
  Bridgeport CNC Mill
  HAAS CNC Mill
Multi-Axis
  HAAS CNC Mill
Lathe
  HAAS CNC Lathe
UI has 3-Axis HAAS and Bridgeport CNC mill machining and limited HAAS lathe capability with CATIA.
Notes: Pics of Mills

## Slide 5: Machine Process Overview
CATIA Product Definition
Create a Machine Plan
Creating a Process Document inside CATIA
  Part Operation Set-up
  Tool Selection
  Machine Operation/Simulation
Verification
Post Processing
Export to CNC mill

## Slide 6: Inside CATIA
CATIA Product
  Part
    Finished product in proper orientation
  Stock
    If necessary
  Fixture
    If necessary

## Slide 7: Guidelines for Creating a Machine Plan
Name, Date, Part, Material, Group, Project, Tolerances, etc.
Stock Size
Sequence Description
Tool List
Picture of Setup
Other Information

## Slide 8: Creating a Process Document
Select Product intended for machining
  Enter Advanced Machining workbench
    Start>Machining>Advanced Machining
PPR
  Process List
    Machine Operation
  Product List
    Part
    Stock
    Fixture
  Resource List
    Tools

## Slide 9: Part Operation| Setup
Define
  Machine
    3-axis mill
  Part
    The finished part
  Stock
    The starting material
  Fixture
    Any clamps or other surfaces not waiting to be machined

## Slide 10: Machine Operation Details
Operation Name
Comment
Tabs
  Machine Strategy
  Geometry
  Tool
  Feeds and Speeds
  Macros
Stoplights
  Colors
    Red – Needs defined
    Yellow – Could be defined, but not necessary
    Green – Defined
Selectable Objects and Text
  Blue text is editable

## Slide 11: Machine Operation| Geometry Colors
Geometry Colors
Red- Not defined and required.
Orange- Not defined, but not required.
Green- Defined.
Brown-Definition element has been changed or deleted.
Purple- Tool path needs to be recalculated.
Blue- Editable parameters.
All surfaces are defined by clicking in the window and then selecting the surface in the geometry

## Slide 12: Questions?