## Slide 1: NC LATHING
By:
Matt Mihelish
Joe Winston

## Slide 2: Overview
NC Geometry
Stock
Part
Product from NC Geometry, Stock, & Part
Lathe operations in lathe workbench
  Rough, groove, finish, &thread turning
  Drilling
Simulation
Creating the following during lathing tutorial:

## Slide 3: NC Geometry
A point in space that is zero or ground for operation
This point allows the part and stock to be joined at a common reference point
Creating
  Open New Part
  Click Point button
    This option then creates an X in the
      axis cube seen in the figure to the right

## Slide 4: Stock
The stock provides a desired form for lathe simulation from which the part is machined.
Creating
  Open New Part
  Draw and dimension desired stock form
  Use pocket tool to generate desired stock length
  Right click on stock and change the transparency in the properties option to 146.
  Change stock to desired color

## Slide 5: Part
Must be a round symmetrical part
Once part is made it must have a profile line defining half the part, this allows for tool path selection
To make a coherent process, i.e. not having to take the part out of the chuck and remount, all tool paths must be accessible from one side

## Slide 6: Part Geometry Creation
Profile
Alignment
Axis
Creating
  Open New Part
  Draw given profile
  Use shaft tool to generate part
  Sketch part profile on ZX axis
  Pocket out a 1” hole through the part center

## Slide 7: Making the Product
Combining NC geometry, stock, and part
  Open a new product and insert components
  Fix NC geometry (anchor button)
  Use contact constraint to constrain stock to NC geometry
  Do the same for the face of the part to the face of the stock

## Slide 8: Final product
All constrained about
Fixed NC geometry
-note all xy planes of
all three parts are
together

## Slide 9: Lathe Machining Workbench
Open Lathe Machining Workbench
  Start Machining Lathe Machining
Open Part Operation
  Process Double click Part Operation
Setup Geometry
  Specify Part
  Specify Stock
Specify part
Specify stock

## Slide 10: Machining lathe work bench
Specify tool change point
Setup Operation
  Adjust tool change position as needed

## Slide 11: Machine Editor
Horizontal lathe operation
Axis specification
Other things of note
-rotation type
-rotation direction
Setup Machine Option
  Click Machine button
  Click Horizontal lathe
  Adjust axes as needed
Machine
Button

## Slide 12: Adding Operations
Click in the manufacturing program to make an active item
  Insert desired tool process by clicking operation buttons
Order of operation is key for the end simulation to run correctly
  Start with final tool operation and finish with the first tool operation to keep order coherent
Operation Tool Bar

## Slide 13: Operation Layout
The operations should be constructed in the following order:
  Threading
  Groove Finish
  Finish Profile
  Drill Operation
  Groove Turning
  Rough Turning

## Slide 14: Threading
a
b
c
In Fig. a specify part material and end limitations. Fig. (b) specify pitch of thread
needing to be cut. Fig. (c the tool can be specified but wasn’t for this tutorial. Default
tool was used.

## Slide 15: Groove Finish
a
b
c
Fig. a specify profile as shown. Fig. b show the feeds and speeds tab allows for specification of speeds for certain materials and tools Fig. c shows macros, used to minimize movement of the tool while machining.

## Slide 16: Finish profile
Finish paths remove excess material and any scalloping. The tool, spindle speeds, and tool approach won’t change for tutorial during finishing and rough machining, but may during actual machining.

## Slide 17: Drill Operation
a
b
Fig (a) is used to specify drill geometry and drill depth. Depth is changed by double clicking Extension and adjusting specification as desired. Fig (b) is used to change drill bit dimensions or other drill bit characteristics. Note: Spindle and feed speeds are default and will be changed during normal operations.

## Slide 18: Rough Turning & Grooving
a
b
Fig (a) depicts the rough turning operation which turns out the entire part profile. The rough turning window requires the selection of the stock and part profile. All other operations such as spindle speed, tool approach were kept at the default setting for this operation.
Fig(b) depicts the groove operation enabling turning of groove profiles on part. The groove turning window requires both the stock and groove profile to be selected as indicated.

## Slide 19: Final Design Tree
After constructing all operations, the final design tree should look like the following figure.

## Slide 20: Simulation
Simulating the machining process requires double clicking the Manufacturing Program 1. The Manufacturing Program 1 box is displayed, by clicking the video camera an animation will commence depicting tool operations.

## Slide 21: Simulation Movie