## Slide 1: ME 433 Internal Combustion Engines
Professor:
Dr. Dan Cordon (AKA Dr. Dan)

## Slide 2
Why Do We Need To Know Fuel Chemistry?
Engine Simulation
We need to balance the chemical equation to figure out the air-fuel ratio of the mixture entering during the intake stroke.
  Find the mass air-fuel ratio for a given equivalence ratio
Mass of air/fuel mixture trapped in the cylinder at the start of the cycle
  We know the volume
  We need the specific volume of the mixture
  We need volumetric efficiency (assumption or measurement)
Need to know how much energy is released during the combustion event
We need to make sure the pre-combustion conditions are not going to cause detonation (auto ignition)
We need to figure out if additional boost pressure is going to results in an increase in power output or not

## Slide 3
Balancing Chemical Equation
For a stoichiometric reaction of hydrocarbon fuel in air we have:
Balance the Carbon to find b
Balance the Hydrogen to find c
Balance the Oxygen to find a
Balance the Nitrogen to find d
If you have a known (lean) equivalence ratio, then the actual reaction is:
Use known equivalence ratio and ‘a’ from stoichiometric reaction
Balance Oxygen to find e
Balance Nitrogen to find f

## Slide 4
Specific Volume for Mixtures
If the intake stroke includes both air and fuel entering you need to calculate the specific volume of the mixture.
For air-fuel ratios greater than 10:1 the change in specific volume may not be worth calculating. In that case simply use the specific volume of air at the inlet pressure and temperature.
You can do this on paper, but software like EES becomes necessary as soon as you consider the change in mixture temperature due to evaporation of fuel (sometimes called chemical intercooling).
If doing this by hand, approximate the specific volume of everything at the ambient temperature.
  Need to use mole fractions of air and fuel (which are the same as the volume fraction or the partial pressures)
  Your balanced reaction included 1 mole of fuel and either a*4.76 moles of air or (1/phi)*a*4.76 moles of air

## Slide 5
First Law Analysis for Reacting System
Consider a constant pressure process in which nf moles of fuel react with
na moles of air to produce np moles of product:
Applying First Law with state 1 being the reactants at P1, T1 and state 2
being products at P2, T2:
Reactants
Products
Reactants
Products
Reaction
State 1
State 2
Q
W

## Slide 6
Enthalpy of Reaction
Consider the case where the final temperature of the products is the same as the initial temperature of the reactants (e.g., calorimeter is used to measure Q).
Reaction
Q
W
P1=P2=Po
T1=T2=To
The heat released under this situation is referred to as the enthalpy of
reaction, DHR ,
To

## Slide 7
The maximum amount of energy is released from a fuel when reacted with a
stoichiometric amount of air and all the hydrogen and carbon contained in the
fuel is converted to CO2 and H2O
This maximum energy is referred to as the heat of combustion or the heating
value and it is typically given per mass of fuel
Heat of Combustion
DHR(298K)

## Slide 8
Heat of Combustion
There are two possible values for the heat of combustion that can be calculated
depending on whether the water in the products is taken to be in a liquid or
vapour state.
Tp
T
S
hg
hf
From steam tables:
hfg = hg – hf > 0
DHR = HP – HR < 0 (exothermic)
The term higher heat of combustion is used when the water in the products is taken to be in the liquid state
The term lower heat of combustion is used when the water in the products is taken to be in the vapor state

## Slide 9
Calculating Heat of Reaction
This example will use a stoichiometric mixture of Methane and air
Balance Carbon
Balance Hydrogen
Balance Oxygen
Balance Nitrogen

## Slide 10
Calculating Heat of Reaction
Calculate enthalpy of products and enthalpy of reactants
LHV = h(products) – h(reactants)
H(products) =  (chemical coefficient * species enthalpy) for products
H(reactants) =  (chemical coefficient * species enthalpy) for reactants
Hproducts
Get the enthalpy of each species at 298 [K] from Table A.4
Use the molar coefficients from the balanced equation above

## Slide 11
Calculating Heat of Reaction
Hreactants
Get the enthalpy of each species at 298 [K] from Table A.4
Get the enthalpy of fuel from Table A.3

## Slide 12
Calculating Heat of Reaction
Calculate enthalpy of products and enthalpy of reactants
LHV = h(products) – h(reactants)
h(products) =  (chemical coefficient * species enthalpy) for products
h(reactants) =  (chemical coefficient * species enthalpy) for reactants
h(products) = 1*(-393.5) + 2*(-241.8) + 2*3.76*(0) [MJ/kmol]
h(reactants) = 1*(-74.52) + 2*(0) + 2*3.76*(0) [MJ/kmol]
Heat of Reaction = -877.1 + 74.5 = -802.6 [MJ/kmol]
Or, per kg of fuel use the molecular mass of the fuel to get:
LHV = -802.6 [MJ/kmol] * [1kmol/(12+4*1)kg] = -50.2 MJ/kgfuel
This is the Lower Heating Value (LHV) because the enthalpies of both products and reactants are in the vapor phase.
Table A.3 has “Calorific Value” for stoichiometric combustion at 298 K, and our calculation matches almost exactly

## Slide 13
Calculating Higher Heating Value
The Higher Heating Value (HHV) can be found by the LHV and adding in the enthalpy of phase change for the water in the products
For example: Find the HHV of Propane
h(products) = 3*(-393.5) + 4*(-241.8-43.99) [MJ/kmol]
** The enthalpy of H2O is reduced by 43.99 MJ/kmol**
h(reactants) = 1*(-104.7) + 2*(0) + 2*3.76*(0) [MJ/kmol]
HHV = -2324 + 104.7 = -2219 [MJ/kmol]
HHV = -2219 [MJ/kmol] * [1kmol/(3*12+8*1)kg] = -50.4 MJ/kgfuel

## Slide 14
Heat of Reaction Activity Follow-Up
Calculate enthalpy of products and enthalpy of reactants
LHV = h(products) – h(reactants)
h(products) =  (chemical coefficient * species enthalpy) for products
h(reactants) =  (chemical coefficient * species enthalpy) for reactants
Heat of Reaction = units of [MJ/kmol_fuel]
Multiply by to get:
  Heat of Reaction = Units of [MJ/kg_fuel]
  Enthalpy change from combustion from each kg of fuel
Multiply by to get:
  Heat of Reaction = Units of [MJ/kg_mixture]
  Enthalpy change from combustion from each kg of air-fuel mixture

## Slide 15
Heat of Reaction Activity Follow-Up
Calculate enthalpy of products and enthalpy of reactants
For Propane
h(products) = 3*(-393.5) + 4*(-241.8) [MJ/kmol]
h(reactants) = 1*(-104.7) + 2*(0) + 5*3.76*(0) [MJ/kmol]
LHV = -2147 + 104.7 = -2042 [MJ/kmol_fuel]
LHV = -2042 [MJ/kmol] * [1kmol/(3*12+8*1)kg] = -46.4 MJ/kg_fuel
For Nitromethane
h(products) = 1*(-393.5) + 1.5*(-241.8) [MJ/kmol]
h(reactants) = 1*(-74.7) + 1.5*(0) + 1.5*3.76*(0) [MJ/kmol]
LHV = -756.2 + 74.7 = -681.5 [MJ/kmol_fuel]
LHV = -681.5 [MJ/kmol] * [1kmol/(1*12+3*1+1*14+2*16)kg] = -11.2 MJ/kg_fuel
Isn’t Nitromethane supposed to make more power?!!!

## Slide 16
Heat of Reaction Activity Follow-Up
Calculate enthalpy of products and enthalpy of reactants per kg_mix
For Propane
LHV = -2147 + 104.7 = -2042 [MJ/kmol_fuel]
MW_mix = kmol_fuel/((3*12)+(8*1)+(5*32)+(5*3.76*28))kg_mix
MW_mix = 730.4 [kmol_fuel/kg_mix]
LHV= -2042 [MJ/kmol] / 730.4 [kmol_fuel/kg_mix]
LHV= -2.79 [MJ/kg_mix]
For Nitromethane
LHV = -756.2 + 74.7 = -681.5 [MJ/kmol_fuel]
MW_mix = kmol/((1*12)+(3*1)+(1*14)+(2*16)+(0.75*32)+(0.75*3.76*28))kg_mix
MW_mix = 163.96 [kmol_fuel/kg_mix]
LHV = -681.5 [MJ/kmol] / 163.96 [kmol_fuel/kg_mix]
LHV= -4.15 [MJ/kg_mix]

## Slide 17
Heat of Reaction Activity Follow-Up
How do we calculate energy released for combustion engine?
Calculate LHV for the fuel [MJ/kmol_fuel]
Calculate LHV for the mixture [MJ/kg_mix]
Calculate specific volume of the mixture [ft^3/lbm]
Use cylinder displaced volume and volumetric efficiency divided by mixture specific volume to calculate mass of mixture in the cycle
Calculate heat released by: LHV_mix * m_mix
EES Code Comparing Methanol and IsoOctane

## Slide 18
Notes from EES Code
Changing from stoichiometric mixture of gasoline to stoichiometric mixture of methanol (with no other changes) *should* slightly increase power output. Our EES code says otherwise (34% decrease in energy released).
Things we didn’t account for:
Inlet temperature (chemical intercooler)  Methanol will be much cooler
Heat of reaction for actual temperature change from products to reactants  Methanol exhaust should be MUCH cooler
Mass burn rate differences  methanol will burn slightly faster, so the efficiency of the actual thermodynamic cycle will be higher for the methanol engine.
Lower combustion temperature means less heat transfer (waste heat) during expansion stroke  greater efficiency
Changes you would make if you were changing fuels
Methanol has an average octane of 119, where gasoline is more like 91.
Increase static compression ratio  cycle efficiency improves
Changes to ignition timing  cycle efficiency improves

## Slide 19
Other Fuel Choices
Alcohol fuels have a ‘OH’ branch that replaces a regular H for hydrocarbon fuels.
Alcohol Notes:
Intake charge cooling from higher evaporation phase change
Lower stoichiometric air-fuel ratio – more fuel means more fuel to burn (but much lower fuel economy if measured in MPG)
Lower combustion temperatures  less waste heat
Alcohol fuels can form small amounts of aldehydes (acetaldehyde, formaldehyde, etc.) in the exhaust. We do *not* want these in our groundwater.
Hydrogen Notes:
Hydrogen has an average octane of over 130
Much higher autoignition temperature than gasoline
Low density makes storage and injection difficult
High diffusion makes manifold or port injection somewhat unsafe
No carbon, so no CO2 emissions.
Similar flame temperature to gasoline, so NOx emissions can still be formed
4x faster flame speed!!