Mechanical Engineering Machine Shop Safety and Orientation Training

JULY 23, 2013

Shop Safety

- Safety glasses are required at all times in the shop.

- No one is allowed to work in the shop in sandals or short pants.

- Don’t wear jewelry around moving equipment.

- Long hair must be tied back.

- Roll up long sleeves around moving equipment.

- 6.  Ear protection, goggles, face shields, shop coats, and first-aid kit are available
     in the shop.

- 7.  Be careful when handling vises, rotary table, indexer, chucks, or other heavy
     items to avoid dropping or back injuries.

- 8.  Do not direct compressed air toward skin.

- 9.  Remember – round things roll.

- 10.  Shop is not properly equipped to handle sawdust or paint fumes.

- 11.  If unsure How or Why – ASK!

- 12.  Regular shop hours – 8:00-11:30, (11:30-12:30 Lunch), 12:30-5:00 Monday-Friday

- Summer shop hours – 7:30-11:30, (11:30-12:30 Lunch), 12:30-4:30 Monday-Friday

Cleanup

1.  Brush chips off entire machine after each use.  Shop-vacs can be used when chips
     are NOT long and stringy.

2.  Do NOT use compressed air to blow chips off machines.

3.  Wipe down machine with shop towels.

4.  When using Koolmist coolant on milling machines, remove vises to clean off
     trapped coolant. This prevents rusting.  Spray vice and mill with WD-40.

5.  Sweep floor in affected area; Do not allow excess chips to build up on floor because
     they will migrate around the shop.

6.  Mop floor if necessary to remove oil or coolant. Mop is located in welding area
     along with soap.

7.  Put used shop towels in metal canister.  Shake out ALL chips first.

8.  Put ALL tools back in the proper place.

Welding Area

- Usage

- Undergrads may use the welding area without a mentor after they
have received appropriate training. Check with shop supervisor first.

- Pedestal grinder

- Do not grind aluminum

- Do not wear gloves while grinding.

- Bead Blaster

- Turn off air after each use.

- Do not bead blast oily or greasy parts.

- Welders

- Make sure the machines are set up according to the charts on the wall before welding.

- If you are not sure about the setting, ask shop manager or mentor first.

- Gas Cylinders

- Let shop manager know when tanks are getting low (200 psi) so replacement
tanks can be ordered.

- Cleanup

- The welding area must be cleaned after each use.

Mills and Lathes

- Always  requires and shop mentor for use

- Your Mentor will go through more training before use

- Must have a machine plan before use

- Must sign up for time on machine with mentor

- Mill and Lathe operations

- Manual vs CNC machines

- Must have any CNC code ready before using CNC machines

  - CNC lathe can use canned cycles or code

Grey Cabinets

These two cabinets (#2 and #3) contain tools and supplies available for shop usage.

Shop towels and cutting oil are located on top of these cabinets.

Tool sign-out sheet – Tools must be signed out if taken out of shop, except when used
                                    in the design suite.  Tools should be returned by COB each day.

Russ’s Area

This area including Bridgeport mill, tool boxes, cabinets, corner area is generally off -limits to students.

Light Brown Cabinet #5

This cabinet contains measuring tools available for shop use.

Drill Presses

- Clamp parts before drilling, especially small or thin parts, such as sheet metal.

- Use cutting oil when drilling.

- Removing chuck or taper-shank drills with drift punches.

- Changing speeds

- Adjusting table heights.

- Quill stop

- T-nuts for Wilton drill press.

- Clamping the work piece

- Do not use end mills in the drill press

- When using cobalt drills, use high speed steel settings, not carbide for RPM’s.

Belt Sander

- Do NOT use gloves while sanding.

- Do NOT force parts into belt.

- Parts can get caught between plate and belt.

- OK for ferrous and non-ferrous materials

- Clean after each use.

Vertical  Band Saw

1.  Select the proper blade for your application as follows:

- 6-tooth blade for aluminum, brass, plastics

- 18-tooth blade for steel and stainless steel

- 24-tooth blade for ALL materials that are 1/8” or less (Especially steel and                                                                     stainless steel)

The 6-tooth and 24-tooth blades are stored at the back of the band saw.

2.  If necessary, install the correct blade in the band saw.

3.  Set the blade tension.

4.  Make sure that the blade guard is in place.

5.  Adjust the upper blade guard so that it is about ¼” above the part to be cut.

6.  Make sure that the band saw is set to the proper speed.
     NOTE: THE MACHINE MUST BE RUNNING TO CHANGE SPEEDS!

7.  Use constant, firm pressure when sawing.  Don’t try and force the work piece through
      too fast.  This may cause teeth to be stripped off the blade.  There is a tube of wax
      that can be used for lubrication.  Just press the tube into the saw blade while it is
      running and it will coat the blade.

8.  When finished with the saw, make sure the blade for cutting steel is installed and
      the speed is set for steel.

9.  Clean the band saw

10.  If you are not sure of something, please ask before proceeding.

Horizontal Band Saw

- Clean after each use.

- Use of coolant

- Speed setting (Adjust only when running)

- Always leave machine set for cutting steel when done with saw.

- Setting vise for angle cuts (Square up to blade after sawing angles)

- Stock stop

Drilling

Center drilling

- Select a center drill similar in size to drill bit.

- RPM is relative to average diameter of tip and body sizes.

- Use cutting oil

Drilling

- Holes up to ½” diameter do not have to be stepped up in size.

- Holes over ½” diameter should be stepped up roughly every ¼” in size.

- When drilling holes to be tapped – refer to chart in shop for drill size.

- When drilling holes to be reamed – leave 1/64” for reaming holes under  ½”, 1/32” for reaming holes every ½”.

- Use cutting oil when drilling.  Koolmist may also be used but it tends to run off immediately.

- When drilling acrylic, stick-wax or cutting oil both work best.

- Coolant not necessary for drilling cast iron.

- When drilling stainless steel, cobalt drill bits work best.

- When drilling sheet metal, always use Uni-bits.

- Make sure parts are properly clamped.

Drills Available

- Number drills - #1 to #60

- Letter drills – A to Z

- Fractional Drills – 1/16” to ½”

- ½” Shank Drills – 1/16” to ½”

- Morse Taper Shank Drills – ½” to 1 7/16”

- Cobalt drills – up to ½”

- Uni-bits – up to 1”

Demonstration

In kit

- Block with the holes for reaming and counter boring pre-drilled

- Center drill

- .201 drill

- Counter-sink

- ¼-20 tap

- .250 reamer

- ¼” counter bore

Demonstration Part

Process

- Tapped hole

  - Center drill

  - Drill through with .201 drill

  - Counter-sink hole

  - Tap hole

- Reamed Hole

  - Ream with .250 reamer

- Counter Bore

  - Counter bore with ¼ counter bore

- Clean up!

RULES FOR STUDENTS WORKING IN

THE MECHANICAL ENGINEERING MACHINE SHOP

All STUDENTS –

ALL NEW PROJECTS MUST BE APPROVED BY THE SHOP MANAGER.

UNDERGRADUATE STUDENTS -

UNDERGRADUATE STUDENTS MUST COMPLETE THE ‘MECHANICAL ENGINEERING MACHINE SHOP SAFETY AND ORIENTATION TRAINING’ AND HAVE A SIGNED AUTHORIZATION SHEET ON FILE IN THE SHOP. THIS MEANS THAT THOSE STUDENTS CAN WORK ON DRILL PRESSES, BELT SANDER AND PEDESTAL GRINDERS, BAND SAWS, AND WELDERS WITHOUT IEW MENTOR SUPERVISION AS LONG AS THE SHOP MANAGER IS IN THE SHOP.

FULL TIME MENTOR SUPERVISION IS ALWAYS REQUIRED TO WORK ON MANUAL LATHES AND MILLS, CNC LATHES AND CNC MILLS, AND THE SURFACE GRINDER.

GRADUATE STUDENTS-

GRADUATE STUDENTS MUST HAVE COMPLETED APPROPRIATE TRAINING ON THE SHOP EQUIPMENT AND HAVE THE APPROVAL OF THE SHOP MANAGER BEFORE WORKING IN THE SHOP.

IEW MENTORS-

ALL IEW MENTORS MUST HAVE COMPLETED APPROPRIATE TRAINING ON MANUAL MILLING MACHINES, MANUAL LATHES, AND CNC MILLS AND LATHES BEFORE MENTORING UNDERGRADUATE STUDENTS ON THIS EQUIPMENT.  THE SHOP MANAGER SIGNS OFF ON MENTOR TRAINING ON EACH PIECE OF EQUIPMENT.

Authorization for engineering students to begin working in the Mechanical Engineering Machine Shop requires orientation about the following:

___ Shop Safety			___Band Saws

___Cleanup				___Drilling

___Welding				___Tapping

___Tool Storage Cabinets		___Reaming

___Drill Presses			___Counter Sinks

___Belt Sanders			___Counter Bores
___Grinders

A sign-up board is located in the Senior Design Suite (GJ108). Your name and the

mentor’s name must both be on the board with the times signed up for.

15 MINUTE RULE- Any machine that is not being used within 15 minutes

of the sign-up start time is then available to be used by another person.

A sheet with names of all students who have received basic training and are
authorized to work in the shop will be posted at the entrances to the shop. This sheet starts over with a clean slate at the end of each Spring semester.

Authorization means that students can work on drill presses, belt sanders and
pedestal grinders, band saws, and welders without mentor supervision as long
as the shop manager is in the shop.

Full time mentor supervision is required to work on manual lathes and mills,
CNC lathes and CNC mills, and surface grinder.

________________________

Name of trainee (Print)

________________

Name of mentor (Print)

________________

Date