## Slide 1: Lecture 15
Nozzles/Diffusers, Valves, Heat XGERs

## Slide 2: The Laws of the Universe
Conservation of Mass – The Continuity Equation
Conservation of Energy – The First Law of Thermodynamics

## Slide 3: Steam Whistle
6.13 A steam whistle is devised by attaching a simple converging nozzle to a steam line. At the inlet to the whistle, the pressure is 60 psia, the temperature is 600°F, and the velocity is 10 ft/s. The steam expands and accelerates horizontally to the outlet, where the pressure and temperature are 14.7 psia and
500°F. Determine the stem velocity at the whistle outlet. Assume the process is adiabatic, aergonic, and steady flow.

## Slide 4: Throttling Valve
6.19 Wet steam is throttled adiabatically and aergonically from 800 psia to 5 psia and 200°F.
If the inlet and exit velocities and heights are equal, what is the ratio of the exit area to the inlet
area for this device?

## Slide 5: Feedwater Heater
6.30 The steady state, steady flow, adiabatic, aergonic feedwater heater shown is used in an electric power plant. It mixes superheated steam with saturated liquid water to produce a low-quality outflow, in which 10 lbm/s of superheated steam at 80 psia and 500°F is mixed with saturated liquid water at 80 psia. The outlet stream has a quality of 10% at 80 psia. What is the mass flow rate of the saturated liquid water flow stream?