## Slide 1: Lecture 18
Introduction to 2nd Law and Entropy

## Slide 2: Example – Hand Calculations
Consider an adiabatic compressor steadily moving R125,
Result: A compressor that compresses a refrigerant and delivers power!  Do you believe this exists?

## Slide 3: Example – EES Calculations
Consider an adiabatic compressor steadily moving R125,
I did it in EES. Now is this believable?

## Slide 4: The Second Law of Thermodynamics
The First Law analysis is correct!
  The First Law is an energy book keeper
The Second Law is not being obeyed!
  The Second Law is the energy transformation police
Before you invest in the contraption on the previous slide, recall the Second Law of Thermodynamics.
Energy can only be transformed. The transformation of energy always proceeds from a condition of very useful energy to less useful energy.
The Second Law dictates how energy can be transformed.
Conclusions with the compressor example …

## Slide 5: What is Entropy?
A thermodynamic property
  Total entropy = S (Extensive - upper case letter)
  Specific entropy = s (Intensive - lower case letter)
An indication of molecular disorder
  High values = high molecular disorder
    Gases
  Low values = low molecular disorder
    Solids
A quantity that can be produced but not destroyed within a system undergoing a process
  Entropy is not a conserved quantity!

## Slide 6: What is Entropy?
Entropy is produced any time there are irreversibilities
  Mechanical friction, fluid friction, heat transfer, mixing, electrical resistance, chemical reactions ...
  Irreversibilities are present in all real-world systems and processes
What is a Reversible process?
  Free of entropy production
  Do not exist – they are idealizations
The Third Law of Thermodynamics
  The entropy of a perfect crystalline substance at absolute zero is zero!
  Provides a universal datum state for entropy

## Slide 7: Why Do Reversible Calculations?
They are EASY!
  Ignore all the hard stuff.
  If a process is reversible, the specific entropy change will be zero.
  Iso-entropy  isentropic
Model Theoretical Limitations
  Simple to calculate maximum theoretically possible performance of a system
  Quick check to back up your B.S. meter
Starting Point for Non-Reversible Calculations
  Isentropic Efficiency  Comparing actual device performance to its maximum theoretical performance
  If you know reversible efficiency and isentropic efficiency you can calculate actual device efficiency using:
Second Law Efficiency
First Law Efficiency

## Slide 8: The Second Law Pioneers
Rudolph Clausius
(1822-1888)
Sadi Carnot
(1786-1832)
William Thomson
(Lord Kelvin)
(1824-1907)
William Rankine
(1820-1872)
Carnot Cycles
Defined Entropy

## Slide 9: The Kelvin-Planck Statement
It is impossible to construct a device that operates in a thermodynamic cycle and delivers a net amount of energy as work to its surroundings while receiving energy by heat from a single reservoir.
Thermal
Reservoir
This is impossible!
C
Implication: No heat engine can ever operate with an energy conversion efficiency of 100%

## Slide 10: Carnot’s Heat Engine
The energy conversion (thermal) efficiency of an irreversible heat engine is always less than the thermal efficiency of a reversible heat engine operating between the same thermal energy reservoirs
All reversible engines operating between the same thermal energy reservoirs will have the same thermal efficiency
  The reversible engine is not dependent on the working fluid
Carnot hypothesized ...
E

## Slide 11: Analysis of the Carnot Heat Engine
Kelvin and Rankine suggested that,
Therefore, the thermal efficiency of a Carnot Heat Engine is,
Temperatures must be on the absolute scale!
E
This is the maximum theoretical efficiency of a heat engine!

## Slide 12: The Clausius Statement
It is impossible for any system to operate in such a way that the energy transfer by heat from a cooler body to a hotter body occurs (without a work input).
System
Cold
Hot
This is impossible!
“Heat always flows down a temperature hill” - Gerald Sielaff (1966)

## Slide 13: Carnot’s Refrigerator
The thermal efficiency of an irreversible refrigerator is always less than the thermal efficiency of a reversible refrigerator operating between the same thermal energy reservoirs
Reversible refrigerators operating between the same thermal energy reservoirs have the same thermal efficiency
  The reversible refrigerator is not dependent on the working fluid
Carnot hypothesized ...
R

## Slide 14: Analysis of the Carnot Refrigerator
For the Refrigeration cycle …
For the Heat Pump cycle …
R

## Slide 15: Thinking like Clausius
My colleagues, Kelvin and Rankine, have proposed that for a Carnot heat engine,
I can rewrite this expression as,
An alternative way to write this is,

## Slide 16: Thinking like Clausius
I have to remember that these expressions have been developed for a Carnot cycle. Since we are considering a cycle that is reversible, it must be true that,
I know that if the cyclic integral of a differential quantity is zero, the quantity must be a property. Therefore, it must be true that,
is the differential of a property!

## Slide 17: Thinking like Clausius
I know that dQ is not a property, but (dQ / T ) for a reversible process is a property! Since I discovered this property, I choose to call it entropy and give it the symbol, S. Therefore,
In 1865, Clausius wrote,
“We might call S the transformational content of the body, just as we have termed the quantity U the heat and work content of the body. But since I believe it is better to borrow terms for important quantities from the ancient languages so that they may be adopted unchanged in all modern languages, I propose to call the quantity S the entropy of the body, from the Greek h troph, meaning a transformation.”

## Slide 18: The Inequality of Clausius
Clausius demonstrated that for a closed reversible process,
It can be shown that for a closed irreversible process (Sec 7.7)
Therefore, for any closed process,
This is known as the Inequality of Clausius