## Slide 1: Lect 27b
Jet Aircraft Propulsion

## Slide 2: Aircraft Propulsion
Thrust produced by increasing the kinetic energy of the air in the opposite direction of flight
Slight acceleration of a large mass of air
  Engine driving a propeller
Large acceleration of a small mass of air
  Turbojet or turbofan engine
Combination of both
  Turboprop engine
2

## Slide 3: Aircraft Gas Turbine Engines
Turboprop
Small commuter planes
Turbojet
high speeds
3
Turbofan
Larger passenger airliners

## Slide 4: The Turbojet
Ideal Turbojet
Ram effect - pressure rise with deceleration
Pressure drop with acceleration
a-1 Isentropic increase in pressure (diffuser)
1-2 Isentropic compression (compressor)
2-3 Isobaric heat addition (combustion chamber)
3-4 Isentropic expansion (turbine)
4-5 Isentropic decrease in pressure with an increase in fluid velocity (nozzle)

## Slide 5: The Turbojet with an Afterburner
The turbine exhaust is already hot. The afterburner reheats this exhaust to a higher temperature which provides a higher nozzle exit velocity

## Slide 6: Turbojet Irreversibilities
Isentropic efficiencies
- Diffuser
- Compressor
- Turbine
- Nozzle
Fluid Friction effects
- Combustion chamber

## Slide 7: The Turbojet Model
First Law analysis of the components in the cycle
Air is the working fluid throughout the complete cycle
Combustion is replaced with a heat transfer

## Slide 8: Turbojet Performance
Propulsive Force (Thrust)
  The force resulting from the velocity at the nozzle exit
Propulsive Power
  The equivalent power developed by the thrust of the engine
Propulsive Efficiency
  Relationship between propulsive power and the rate of kinetic energy production
There is no net power output of the turbojet engine. Therefore, the idea of net power and thermal efficiency are not meaningful. In turbojet engines, performance is measured by,

## Slide 9: Turbojet Performance
Propulsive Force (Thrust)
Propulsive Power
The power developed from the
thrust of the engine
in (a)
exit (5)
In this equation, the velocities are relative to the aircraft (engine). For an aircraft traveling in still air,

## Slide 10: Turbojet Performance – Efficiencies
Overall Efficiency
Thermal Efficiency
Propulsive Efficiency
Kinetic energy production rate
Thermal power available from the fuel
Kinetic energy production rate
Propulsive power

## Slide 11: Turbojet Example
Given: A turbojet engine operating as shown below
Find:
The properties at all the state points in the cycle
The heat transfer rate in the combustion chamber (kW)
The velocity at the nozzle exit (m/s)
The propulsive force (lbf)
The propulsive power developed (kW)
The propulsive efficiency of the engine

## Slide 12: Turbojet Example
Note: An array position of [0] is allowed in EES!

## Slide 13: Turbojet Example
Strategy: Build the property table first. This will require some thermodynamic analysis. Consider each component in the cycle.
Diffuser

## Slide 14: Turbojet Example
Compressor
Combustion Chamber
Turbine

## Slide 15: Turbojet Example
Nozzle
At this point, the property table is complete!

## Slide 16: Turbojet Example
Now, we can continue with the rest of the thermodynamic analysis.
Nozzle – Exit Velocity
Combustion Heat Transfer Rate

## Slide 17: Turbojet Example
Now the propulsive parameters can be calculated,

## Slide 18: Turbojet Example
Solution (Key Variables):

## Slide 19: Turbojet Example – Analysis
How is the energy input to this engine distributed?
excess thermal energy transfer
kinetic energy production rate