ME529 Combustion and Air Pollution

Topic 04a.  Combustion Thermodynamics

4.1 Energy Balance to Obtain Heat of Combustion

The 1st law of thermodynamics (energy balance) applied to a closed system (no mass transfer):

where we use the convention of heat transfer to the system as positive, and work done by the system as negative.

If  KE and PE are = 0,

or

If the work done is compression or expansion, the energy needed to change volume by dV at pressure p is -pdV and

Note that the change in internal energy is the change in heat transfer for constant volume systems.

For convenience, the state function enthalpy is defined as

or

Substituting in the 1st law, and the expression for enthalpy becomes

Note that the change in enthalpy is the change in heat transfer for constant pressure systems.

For open (flow-through) systems,

For a chemical reaction:

where the ('s are the stoichiometric coefficients of the chemical compounds.  The LHS are reactants; the RHS are products.

Conservation of mass:

Conservation of energy:

where hi(T) is the enthalpy or heat of formation of species i.  The heat transfer per mole that is required to maintain the process at a constant temperature T is called the enthalpy of reaction.

The enthalpy of species i is defined relative to a reference state where the enthalpy is taken to be zero.  This reference state is To = 298 K and Po = 1 atm = 101 kPa, or reference temperature and pressure (RTP), and is based on the pure elements in a chemically stable state at To and Po; C is solid graphite, H exists as H2 gas, N as N2 gas, O as O2 gas, S as solid sulfur, and so on.  Hence, the enthalpy of a compound like water at the standard state (RTP) is its enthalpy of formation:

H2 + 1/2 O2 ===> H2O

The enthalpy of formation is the energy released or absorbed when the compound is formed from its elements (with reactants and products all at RTP).

The superscript o denotes reference to the chemical reference state.  The enthalpy of formation of pure elements at the reference state is zero (see the table in the attached appendix).

Figure 1.  Enthalpy of formation.

In Figure 1, C and oxygen enter a reactor and react completely at steady state to form carbon dioxide at the same T and P.  Carbon dioxide is formed according to

C + O2 <===> CO2

This reaction is exothermic so heat must be transferred from the reactor to the surroundings for the products to exit at the same temperature and pressure.  An energy balance yields:

Here, is the molar flow rate and  is the enthalpy per mole.   Solving for the enthalpy of carbon dioxide and noting that, from the reaction equation, all molar flow rates are the same,

Since C and O2 are stable elements at RTP,  = 0 and = 0.  Hence, the specific enthalpy of carbon dioxide at RTP is the heat transfer per mole of CO2, between the reactor and the environment.  It is -394,088 kJ per kmol of CO2 formed.  (The sign is -ve because it is heat transferred FROM the reactor, exothermic.  (If heat must be transferred TO the reactor, the reaction is endothermic.)   This energy is the enthalpy of formation and is tabulated in the table in the attached appendix as well as in the JANAF Thermochemical Table, NASA database, thermodynamics textbooks, chemistry texts, etc.

The enthalpy of a compound at any temperature is the sum of the enthalpy of formation at To and a sensible enthalpy term associated with the (T from To to T:

The sensible enthalpy is the integral over temperature of the specific heat at constant pressure:

In combustion systems, the variation in Cp cannot be ignored because of the large range in temperature.  A linear approximation to Cp is:

The values of a and b for species important in HC combustion are listed in the table in the attached appendix.  Use of tabulated enthalpies or those calculated from tables in programs like EES or ALLPROPS is far more accurate.  STANJAN and the NASA equilibrium code, which we will use later, use data from the JANAF tables.

A much more accurate polynomial representation for specific heat is given in the NASA thermodynamic databases (also used by the Chemkin program).  Appendix A.13 on pages 646 – 647 in the class textbook lists some of these coefficients.  The complete database can be downloaded from the class webpage.

We can now apply the 1st law of thermodynamics in a chemically reacting open system.

________________________________________________________________

Example 4.1 - Methane gas at 400 K enters a combustion chamber, where it is mixed with air entering at 500 K and 1 atm.  The products of combustion exit at 1800 K and 1 atm.  For steady state operation, determine the rate of heat transfer from the combustion chamber in kJ per kmol of fuel.  Neglect KE and PE effects.

Assume:  1) no work done by/on SSCV; 2) ignore KE & PE effects; 3) reactants and products can be modeled as ideal gases; 4) atmospheric nitrogen is inert.

Solution:

First, balance the combustion reaction (conservation of moles).

CH4 + 2 (O2 + 3.78 N2) ===> CO2 + 2 H2O + (2 x 3.78) N2

The conservation of energy reduces to:

Note that  for O2 and N2 (on both sides of the reaction) is = 0.

Substituting in values from the table in the appendix:

Perform the integrations:

Combine all terms:

________________________________________________________________

4.2 Higher and Lower Heating Values

The chemical composition of many practical fuels is not known.  Also, the enthalpy data must be known for ALL the reactants and products to calculate the enthalpy of combustion.  Otherwise, the enthalpy of the combustion reaction must be obtained experimentally in a calorimeter.  Both flow calorimeters and constant-volume (bomb) calorimeters usually measure the higher heating value (HHV) of a fuel.  Engineers need to distinguish between HHVs and the lower heating value (LHV) of fuels.

The HHV includes the heat of vaporization of water vapor formed during combustion because it assumes that all of the water in the combustion products has condensed to liquid.  The LHV assumes that all of the products of combustion remain gaseous.

When experiments are done at room temperature in the calorimeter (that is, reactants start out at 298 K and reactants are cooled to 298 K), water vapor formed during combustion will condense.  This increases the apparent heat release due to the latent heat of vaporization.

Since exhaust temperatures are usually high enough to prevent condensation, the LHV is more relevant.  Hence, when the HHV is given, it often needs to be converted into a LHV.

LHV = HHV - n hfg,H2O

________________________________________________________________

Example 4.2 HHV and LHV

The HHV of a fuel oil with the molecular formula CH2.186 is measured as -44,135 J/g.  Calculate the LHV in kJ/mol.

Solution:  The latent heat of vaporization at 298 K for water is -43,961 J/mol.

LHV = -44,135 J/g x (12 + 2.186) g/mol- 2.186/2 g/mol x ( -43,961) J/mol

= -626,099 J/mol + 48,049 J/mol = - 578 kJ/mol

________________________________________________________________

4.3 Adiabatic Flame Temperature

The maximum exhaust temperature from a combustor could be achieved if none of the heat released was lost to the walls of the burner, and if combustion were stoichiometric, complete, and there was no dissociation of products.  The temperature achieved by this adiabatic, ideal combustion is called the adiabatic flame or adiabatic combustion temperature.  The adiabatic flame temperature can be calculated using conservation of mass and conservation of energy.   Assume that the combustion air and combustion products form ideal gas mixtures.  Since all heat transfer is internal, the energy balance reduces to

or

The number of moles (n) are obtained from the balanced chemical reaction.  The enthalpy of formation of products is tabulated.  Enthalpy of combustion data might have to be used when the enthalpy of formation of the fuel is not known.  The  terms for the reactants can be evaluated from Cp data.  The unknown adiabatic flame temperature appears implicitly and hence must be solved for iteratively.  A program such as STANJAN, EES or Mathcad can be used, or even a spreadsheet can be set up for manual iterative calculations.  Alternatively, a computer program could be written.

References

Flagan, R. C., and Seinfeld, J.H., Fundamentals of Air Pollution Engineering, Prentice Hall, 1988.

Skull, D. R., and Prophet, H., “JANAF Thermochemical Tables,” 2nd Edition, National Bureau of Standards NSRDS-NBS 37, 1971.

Appendix A.  Approximate Thermodynamic Data for Species of Combustion Interest (Flagan and Seinfeld, 1988)

| Species | Name | (hf( (298 K) (J / mol) | s( (298 K) (J / mol K) | Cp = a + bT ( J / mol K ) |
| --- | --- | --- | --- | --- |
|  |  |  |  | a | b |
| C | Carbon, monatomic | 716,033 | 158.215 | 20.5994 | 0.00026 |
| C (s) | Graphite (ref.) | 0 | 5.694 | 14.926 | 0.00437 |
| CH | Methylidine | 594,983 | 183.187 | 27.6451 | 0.00521 |
| CH2 | Methylene | 385,775 | 181.302 | 35.5238 | 0.01000 |
| CH3 | Methyl | 145,896 | 194.337 | 42.8955 | 0.01388 |
| CH4 | Methane | -74,980 | 183.413 | 44.2539 | 0.02273 |
| CN | Cyano | 435,762 | 202.838 | 28.2979 | 0.00469 |
| CO | Carbon monoxide | -110,700 | 197.810 | 29.6127 | 0.00301 |
| COS | Carbonyl sulfide | -138,605 | 231.804 | 47.6042 | 0.00659 |
| CO2 | Carbon dioxide | -394,088 | 213.984 | 44.3191 | 0.00730 |
| C2H | CCH radical | 447,662 | 207.615 | 40.4732 | 0.00880 |
| C2H2 | Acetylene | 227,057 | 201.137 | 51.7853 | 0.01383 |
| C2H4 | Ethylene | 52,543 | 219.540 | 60.2440 | 0.02637 |
| C2H4O | Ethylene oxide | -52,710 | 243.272 | 70.1093 | 0.03319 |
| C2N2 | Cyanogen | 309,517 | 241.810 | 63.7996 | 0.00913 |
| H | Hydrogen, monatomic | 218,300 | 114.773 | 20.7859 | 0 |
| HCHO | Formaldehyde | -116,063 | 218.970 | 43.3037 | 0.01465 |
| HCN | Hydrogen cyanide | 135,338 | 202.000 | 38.9985 | 0.00885 |
| HCO | Formyl | -12,151 | 245.882 | 37.3667 | 0.00766 |
| HNO | Nitroxyl hydride | 99,722 | 220.935 | 38.2143 | 0.00750 |
| HNO2 | Nitrous acid, cis- | -76,845 | 249.666 | 54.0762 | 0.01100 |
| HNO2 | Nitrous acid, trans- | -78,940 | 249.498 | 54.5058 | 0.1075 |
| HNO3 | Nitric acid vapor | -134,499 | 266.749 | 68.1195 | 0.01549 |
| HO2 | Hyperoxyl | 20,950 | 227.865 | 38.3843 | 0.00719 |
| H2 | Hydrogen (ref.) | 0 | 130.770 | 27.3198 | 0.00335 |
| H2O | Water vapor | -242,174 | 188.995 | 32.4766 | 0.00862 |
| H2O2 | Hydrogen peroxide | -136,301 | 232.965 | 41.6720 | 0.01952 |
| H2S | Hydrogen sulfide | -20,447 | 205.939 | 35.5142 | 0.00883 |
| H2SO4 | Sulfuric acid vapor | -741,633 | 289.530 | 101.7400 | 0.02143 |
| H2SO4 | Sulfuric acid liquid | -815,160 | 157.129 | 144.0230 | 0.02749 |
| N | Nitrogen, monatomic | 476,326 | 153.413 | 20.7440 | 0.00004 |
| NH | Imidogen | 339,392 | 181.427 | 28.0171 | 0.00349 |
| NH2 | Amidogen | 167,894 | 194.785 | 33.5349 | 0.00837 |
| NH3 | Ammonia | -45,965 | 192.866 | 38.0331 | 0.01593 |
| NO | Nitric oxide | 90,421 | 210.954 | 30.5843 | 0.00278 |
| NO2 | Nitrogen dioxide | 33,143 | 240.255 | 43.7014 | 0.00575 |
| NO3 | Nitrogen trioxide | 71,230 | 253.077 | 61.1847 | 0.00932 |
| N2 | Nitrogen (ref.) | 0 | 191.777 | 29.2313 | 0.00307 |
| N2H | Diimide | 213,272 | 218.719 | 43.2755 | 0.01466 |
| N2O | Nitrous oxide | 82,166 | 220.185 | 44.9249 | 0.00693 |
| N2O5 | Dinitrogen pentoxide | 11,313 | 346.933 | 122.4940 | 0.01018 |
| O | Oxygen, monatomic | 249,553 | 161.181 | 21.2424 | -0.0002 |
| OH | Hydroxyl | 39,520 | 183.858 | 28.0743 | 0.00309 |
| O2 | Oxygen (ref.) | 0 | 205.310 | 30.5041 | 0.00349 |
| O3 | Ozone | 142,880 | 239.166 | 43.3802 | 0.00553 |
| S (g) | Sulfur, gas | 279,391 | 168.019 | 22.4619 | -0.0004 |
| S (l) | Sulfur, liquid | 1,425 | 35.364 | 28.5005 | 0.00976 |
| S (s) | Sulfur, solid (ref.) | 0 | 31.970 | 13.9890 | 0.02191 |
| SO2 | Sulfur dioxide | -297,269 | 248.468 | 45.8869 | 0.00574 |
| SO3 | Sulfur trioxide | -396,333 | 256.990 | 62.1135 | 0.00877 |