## Slide 1: ME 433 Internal Combustion Engines Review Session #1
Professor:
Dr. Dan Cordon (AKA Dr. Dan)

## Slide 2: The Laws of the Universe
Conservation of Mass – The Continuity Equation
Conservation of Energy – The First Law of Thermodynamics
The Entropy Balance – The Second Law of Thermodynamics

## Slide 3: First Law for Closed System
Since this is a closed system, the mass must remain constant.

## Slide 4: Closed System Summary
The First Law over a finite period of time is (making a movie),
The First Law at an instant in time is (taking a picture),
Total Form
Specific Form

## Slide 5: Moving Boundary Work
Example: Expansion of a fluid in a piston-cylinder assembly
The work done can be found by integration,
In order to find the work done, the pressure-volume relationship needs to be known. Work is a path function!

## Slide 6: The Polytropic Process
Evaluation of the integral
For the case where
For the case where n = 1,
The polytropic process defines a relationship between end states,

## Slide 7: The Polytropic Process – Ideal Gas
The previous relationship is valid, independent of the fluid,
If the fluid behaves like an ideal gas,
This leads to two additional relationships for ideal gases,

## Slide 8: The Polytropic Process – Ideal Gas
Previously we defined the work done during a polytropic process to be:
However, if the fluid behaves like an ideal gas that relationship can be written as:

## Slide 9: Ideal Gases w/constant cp
We previously derived the following expressions for an ideal gas from the Gibbs Equations,
If the gas is undergoing a process where the heat capacity can be assumed to be constant,
Consider a case where the process is also isentropic.

## Slide 10: Isentropic Ideal Gases w/constant cp
Algebra time ...
Rearrange the exponent,

## Slide 11: Isentropic Ideal Gases w/constant cp
Substitution gives,
Using the other Gibbs equation for an isentropic process
Therefore, for an ideal gas with constant heat capacity undergoing an isentropic process,

## Slide 12: Isentropic Ideal Gases w/constant cp
But wait ... there’s more!!
Rearranging ...
Does this look familiar?

## Slide 13: Polytropic Process Relations
Any fluid model (P-v relationship)
Ideal Gas Model (P-v-T relationship)
Ideal Gas Model – Isentropic process, constant heat capacity
Important Polytropic Exponents

## Slide 14: Calorific Equation of State for Ideal Gas Model
For an Ideal Gas the change in specific internal energy is a function of its change in temperature
Since we are dealing with an ideal gas, pv = RT. Therefore,
This leads to the following conclusion (Balmer section 3.9.2),
It can also be shown (Balmer section 3.9.2) that,

## Slide 15: The Ideal Gas Model
Significance:
These equations allow us to determine internal energy and enthalpy changes for ideal gases. In order to integrate the du and dh equations, we need to determine one of the specific heats.
With ideal gases, the specific heat dependence on temperature may be stronger compared to incompressible substances.
Exceptions: The heat capacities are constant for the inert gases. For the inert gases,

## Slide 16: Analysis of the Carnot Heat Engine
Kelvin and Rankine suggested that,
Therefore, the thermal efficiency of a Carnot Heat Engine is,
Temperatures must be on the absolute scale!
E
This is the maximum theoretical efficiency of a heat engine!

## Slide 17: Analysis of the Carnot Refrigerator
For the Refrigeration cycle …
For the Heat Pump cycle …
R