## Slide 1: Round 1 Debrief - PM
What worked?
  division of folding labor
What didn’t work?
  inspection was slow
  folding was a bottleneck (esp fold 2)
  time spent transporting material
  workers were waiting while others were finishing batch
  re

## Slide 2: Changes for Round 2
Consider the following:
  Factory Layout
    Oven must remain separated
    Place folding operations adjacent to each other
  Point of Use Storage (POUS)
    Fold 1 can grab paper
  Line Balancing
    Send production schedule to Fold 1
    Have only one worker at oven and one stamper
    Evenly distribute folding operations to match Takt time
  Poke-Yoke, Quality at the Source
    Identifying and controlling quality problems is more difficult in parallel operations
    Rework at the source

## Slide 3: Round 2 Debrief - PM
What worked?
  Fold table seemed like a work cell
What didn’t work?
  At each station you need to have visual queue to determine what you need to do and when to do it

## Slide 4: Changes for Round 3
Consider the following:
  Factory Layout
  Pull System, Kanban
    Use silver and gold sheets as Kanban cards (place boats on top of each sheet)
    Set Kanban of 2 silver and 2 gold
    How many boats to store in warehouse
  Continuous Flow and Supermarkets
    Place
  Poke-Yoke, Quality at the Source
    Continue with inspection at each station

## Slide 5: Round 3 Debrief - PM
What worked? What didn’t work?
  Pull system
    Less stressful
    Less late orders
    Know what you’re supposed to make
    You know you’re working on what’s selling
    Easier to see production status
Areas for improvement?
  Kanban size adjustments
    More in inventory (4 to 6 or 8)
  Assembly layout adjustments