## Slide 1: Aluminum
-Color: bright silver grey
-Characteristics: very strong and light, very malleable, corrosion
resistant. Non-magnetic.
-Uses: structural components where strength is necessary but weight is a concern. Do not use for high wear components.
-Machinability: stable, easy to machine at relatively high feeds and speeds without special tools. Welding 5000 and 6000 series alloys requires some skill with TIG welder, 7000 series alloys are not weldable.

## Slide 2: BRASS
-Color: yellow/gold
-Characteristics: electrically conductive, very malleable, corrosion
resistant. Non-magnetic.
-Uses: aesthetic/decorative components, electric/thermal conduction, corrosion resistance. Sometimes used for replaceable low-wear bushings.
-Machinability: easy to machine at relatively high feeds and speeds without special tools.

## Slide 3: COPPER
-Color: reddish gold
-Characteristics: very malleable, corrosion
resistant, electrically conductive. Softer than brass. Non-magnetic.
-Uses: tubing is the most common, also conductive components. Do not use for high wear components.
-Machinability: stable, machinable at relatively high feeds and speeds without special tools. Annealed copper can present machining difficulties due to its softness.

## Slide 4: COLD DRAWN STEEL
-Color: light grey
-Characteristics: very strong, high wear resistance, relatively precise stock size. High internal stresses due to manufacturing process.
Magnetic.
-Uses: components where strength and fairly accurate initial stock size is necessary. Can be used for high wear components.
-Machinability: easy to machine with common tooling (HSS or Carbide), frequently unstable due to relaxation of internal stresses by machining. Easily welded with TIG or MIG.

## Slide 5: HOT ROLLED STEEL
-Color: dark grey/black
-Characteristics: strong, easy to work with. Less precise stock dimensions than cold drawn steel. Rough, scaly surface finish.
Magnetic.
-Uses: components where strength and ease of manufacturing are important.
-Machinability: easy to machine with common tooling (HSS or Carbide), very stable. Easily welded with TIG or MIG.

## Slide 6: FLAT GROUND STEEL
-Color: silvery grey
-Characteristics: extremely precise stock size (±0.015”), very strong (typically oil hardened), ground surface finish. Typically sold/stored in plastic/paper envelopes. Magnetic.
-Uses: often used for cutting tools or other components that require precise dimension tool steel. Extremely wear resistant.
-Machinability: difficult without specialized tools.

## Slide 7: STAINLESS STEEL
-Color: silvery grey
-Characteristics: very strong, good corrosion resistance, relatively precise stock dimensions. Difficult to work with. Non-magnetic.
-Uses: components that require high corrosion resistance, but also require higher strength than aluminum, brass, or copper. Also for some aesthetic components.
-Machinability: difficult without specialized tools. Welding requires some skill with TIG welder.