## Slide 1: Lecture 6
Thermodynamic Diagrams
Phase Change
Determination of Properties with Equations of State (EOS)

## Slide 2: Thermodynamic Diagrams
The P-v Diagram
The P-T Diagram
Phase Diagram
The P-v-T Surface
To view the T-v diagram look at the top view of the P-v-T surface

## Slide 3: Thermodynamic Diagrams
The P-v Diagram
The P-T (Phase) Diagram
Projections of the P-v-T 3D surface

## Slide 4: The State Postulate
Two independent, intensive properties fix the thermodynamic state of a simple substance
Typical Phase Diagram
This state is fixed by T and P which are independent in the single phase. Once the state is identified, all thermodynamic properties of the state are known.
Defines

## Slide 5: The State Postulate
Two independent, intensive properties fix the thermodynamic state of a simple substance
Typical Phase Diagram
This state on the p-T plot is unclear. What phase is the substance in? It’s right on the liquid-vapor line.
Defines

## Slide 6: Phase Change
What if we put a sealed container with a moving piston on the stove? The top side of the piston is exposed to atmospheric pressure.
Start with liquid at T = 72 °F
Add heat  what happens?
How does this look on a T-v diagram?

## Slide 7: Phase Change
What about other pressures?

## Slide 8: What is a Gas? Superheated Vapor?
While Superheated Vapor and Gas may behave similarly, they are defined differently.
Superheated Vapor
  To the right of the Saturated Vapor line
  Temperature  below the Critical Temperature
Gas
  Temperature  above Critical Temperature
  Pressure  below the Critical Pressure
Supercritical
  Temperature  above Critical Temperature
  Pressure  above the Critical Pressure

## Slide 9: T-v Diagram
critical point
L
V
G
SC
Saturated Liquid
Saturated Vapor
L + V

## Slide 10: P-v Diagram
critical point
L
V
G
SC
Saturated Liquid
Saturated Vapor
L + V

## Slide 11: Thermodynamic Nomenclature
Phase | Thermodynamic Name
Liquid | Compressed liquid
Vapor | Superheated vapor
Liquid + Vapor | Wet, Saturated, or 2-Phase Mixture
Gas | Gas
Supercritical | Supercritical
Saturation Property Nomenclature
Saturated liquid properties are signified with a subscript f
Saturated vapor properties are signified with a subscript g
Saturated solid properties are signified with a subscript i
For example ...
f
German: Fussig
Means: Fluid

## Slide 12: Quality – A New Property
p,T are NOT independent in the wet region. However, p,v and T,v are independent.
But, what if you are trying to find v? To do this, I need another independent, intensive property to fix the state of a saturated mixture.
The property we need is the quality, x, of the mixture.

## Slide 13: Quality – A New Property
Consider the total volume of a wet mixture …
Define ...
Therefore ...
Substituting ...
Significance: p,x and T,x are independent, intensive properties in the wet region!

## Slide 14: Quality – A New Property
Quality expressions are valid for other internal energy, enthalpy, and entropy too!
A little algebra ...
Definition!!

## Slide 15: Property Models
The Incompressible Substance Model
The Ideal Gas Model
The Real Fluid Model

## Slide 16: The Incompressible Substance Model
Liquids and Solids

## Slide 17: The Incompressible Substance Model
As seen in the reading (Section 3.9.1),
If we know the value of c (or the variation of c with T), the above equation, du = cdT can be integrated between any two states to determine the change in internal energy. Once the change in internal energy is known, the change in enthalpy can also be found!
It can also be shown (see Section 3.9.1) that,

## Slide 18: The Ideal Gas Model
Gases T >> Tc and P << Pc

## Slide 19: The Ideal Gas Model
As seen in the reading (Section 3.9.2),
Since we are dealing with an ideal gas, pv = RT. Therefore,
This leads to the following conclusion (section 3.9.2),
It can also be shown (section 3.9.2) that,

## Slide 20: The Ideal Gas Model
Significance:
These equations allow us to determine internal energy and enthalpy changes for ideal gases. In order to integrate the du and dh equations, we need to determine one of the specific heats (the other can be found with the third equation).
With ideal gases, the specific heat dependence on temperature may be stronger compared to incompressible substances. Exceptions: The heat capacities are constant for the inert gases. For the inert gases, cp = 5R/2

## Slide 21: The Real Fluid Model
True for the complete P-v-T surface

## Slide 22: The Real Fluid Model
Theoretical extension of the Ideal Gas EOS
  Clausius, van der Waals, Beattie-Bridgeman, Redlich-Kwong (Section 3.9.4)
Theory cannot fully predict correct fluid behavior
  Example: The van der Waals EOS is not valid in the liquid phase!
Modern EOSs include theoretically significant terms, but also have empirical terms to make up the deficiency in theory

## Slide 23: The Real Fluid Model

## Slide 24: The Modified Benedict-Webb-Rubin EOS
A high-accuracy EOS