## Slide 1: Lecture 22
Second Law Analysis of Open Systems
Isentropic Device Efficiency

## Slide 2: Isentropic Efficiency of Devices
Performance index of a device
Comparison of device performance relative to an isentropic process
  The isentropic process is reversible + adiabatic
  The isentropic process represents the limiting performance of the device
    Not achievable in the real-world
    A great benchmark for design and analysis
    Isentropic efficiency can never be > 100%
No general expression
  Device specific

## Slide 3: Variable X___, s
The ‘,s’ seen in each of the following equations represents the ideal exit conditions
Ideal means a case where entropy across the device is constant (no entropy produced).
Isentropic efficiency is used to compare the ‘ideal’ and ‘real’ (or ‘actual’) performance.
In each case, the inlet conditions are the same between the ideal and real cases (same state).
Something about the outlet conditions will also be the same between the ideal and real cases (which variable depends on the device).
The ideal case will always be one where the entropy of the inlet is the same as the entropy of the outlet.
The real case will always have higher entropy at the outlet than the inlet.

## Slide 4: Isentropic Efficiency of Devices
Diffusers
Nozzles
The exit of the isentropic (ideal) nozzle is at the same pressure as the irreversible (real) nozzle
The exit of the isentropic (ideal) diffuser is at the same velocity as the irreversible (real) diffuser

## Slide 5: Isentropic Efficiency of Devices
Turbines
Mollier Diagram

## Slide 6: Isentropic Efficiency of Devices
Compressors

## Slide 7: Isentropic Efficiency of Devices
Pumps
saturated liquid
L
L+V

## Slide 8: Isentropic Efficiency of Devices
What about throttling processes and heat exchangers?
Throttling Process
There is no ‘reversible’ analog to a throttling process. Specifying an ‘isentropic’ throttling results in an enthalpy change across the device. And a delta_h implies work is involved.
Isentropic efficiency doesn’t exist for a throttling device
Heat Exchangers
Heat exchange occurs by virtue of a temperature difference between the objects. By definition: all heat transfer is irreversible.
Isentropic efficiency doesn’t exist for a heat exchanger

## Slide 9: Example – air turbine w/Air Tables
Air expands through a turbine (operating at steady-state) from a pressure of 450 kPa and a temperature of 550 K to an exhaust pressure of 150 kPa. Assume the process is reversible and adiabatic, with negligible changes in kinetic and potential energy.
Sketch the system & boundary and classify the system.
Show initial and final states on both Pv and Ts diagrams.
Use these diagrams to forecast work and heat transfer. (+/-)
Simplify the First Law equation for this process.
Simplify the Second Law equation for this process.
Use the air tables to find properties at initial and final states.
Calculate specific work (w) from the turbine?
Calculate specific heat transfer (q) from the turbine?
What is the specific entropy production (sp) for this turbine?

## Slide 10: Example – steam turbine
A steady-state steam turbine receives steam at a pressure of 1 MPa, 300 °C. Steam leaves the turbine at a pressure of 15 kPa. The specific work output of the turbine is measured and found to be 600 kJ/kg.
Sketch the system & boundary and classify the system.
Show ideal initial and final states (with isobars) on a Ts diagram.
Show real initial and final states on the Ts diagram.
Simplify the First Law equation for this process.
Simplify the Second Law equation for this process.
Use the steam tables to find properties.
What is the quality at the turbine outlet (both real and ideal)?
Calculate the specific work for an ideal turbine.
Calculate the isentropic efficiency of the turbine.
Calculate the specific entropy production for the real turbine.