## Slide 1: Lecture 30
Heat Pump Systems

## Slide 2: Tons of Refrigeration
One ton of refrigeration is the heat transfer rate required to melt 1 ton (2000 lbf) of ice at 32°F in 1 day (24 hr).
What heat transfer rate can accomplish this?
Latent heat of fusion of ice (hf – hs) at 1 atm
Then:

## Slide 3: The Heat Pump Cycle
Performance
The heat pump cycle IS a refrigeration cycle!

## Slide 4: Heat Pumps
How can the high temperature heat transfer be utilized? It all happens at the condenser. A few possibilities are …
Cold air in
Hot air out
Heating Air
Heating Water
Cold water in
Hot water out
Hot refrigerant vapor
Hot condensed refrigerant
Hot refrigerant vapor
Hot condensed refrigerant

## Slide 5: Heat Pumps
Application: Residential heating

## Slide 6: Air-Source Heat Pump
Source
Sink
The heat pump is able to meet the house heating load.
The heat pump is not able to meet the house heating load. An auxiliary heat source is needed.

## Slide 7: Isothermal Source Heat Pump
No auxiliary heat source needed. The heat pump can always meet the house load!
In principle, this is a great idea! However it is cost prohibitive to circulate refrigerant through the isothermal source. R22 ~$20/lbm, R134a ~$8/lbm
Source
Sink

## Slide 8: Isothermal Source Heat Pump
Secondary heat transfer loop
(Some type of glycol mixture)
Evaporator

## Slide 9: Possible Isothermal Sources
The Earth
  In-ground secondary loop needed
    Horizontal loop
    Vertical loop
Ground water from a geothermal well
  Environmental issues?
A contained mass of water
  Ice-making heat pump
Others?

## Slide 10: Heat pumps
Application: Providing both heating and cooling with a heat pump

## Slide 11: Heating and Air Conditioning
The reversing valve reverses the roles of the heat exchangers.

## Slide 12: Reversing (4-way) Valve
Condenser
Evaporator
Evaporator
Condenser
Expansion Valve
Compressor
Heat Pump Mode
Refrigeration (Air-Conditioning) Mode
Qout
Qin
Qin
Qout