## Slide 1: Lecture 31
Ideal Gas Mixtures

## Slide 2: Mixtures in Engineering Applications
Natural gas
  Methane, ethane, propane, butane, nitrogen, hydrogen, carbon dioxide, and others
Refrigerants
  Zeotropes - True mixture behavior
    Example: R407c - R32/125/134a (23/25/52 by mass)
  Azeotropes - Mixtures that behave as a pure fluid
    Example: R507A - R125/143a (50/50 by mass)
Air and water vapor
  Psychrometric analysis
    Air conditioning applications

## Slide 3: Pure Fluid vs. Mixture Behavior
R22: a pure fluid; a halogenated methane molecule (chlorodiflouromethane)
R407C: a mixture of R32, R125, and R134a

## Slide 4: Thermodynamic Properties of Mixtures
Real mixture behavior
  Real mixture model
    Very complex to describe analytically
      Topic for an advanced course
    EES can calculate real-properties of common mixtures!
Low-pressure, moderate density
  Ideal solution model
    Gases are treated as real fluids with idealized mixing
      Topic for an advanced course
Low-pressure, low density
  Ideal gas mixing model
    Gases are treated as ideal gases with idealized mixing
      ME 322!!

## Slide 5: Ideal Gas Mixture Models
Air Conditioning
  Water vapor + air mixtures
    Conditions are suitable for ideal gas property estimation – even for water vapor!
Combustion Analysis
  Products of combustion are often at high temperatures and low pressure
Even though the ideal gas mixing model is simplified, it turns out to be fairly accurate for two important processes that mechanical engineers deal with ...
The rest of ME 322 deals with these two processes

## Slide 6: An Example – Gas Turbines
Air into the combustion chamber
Products of combustion leaving the combustion chamber
Combustion products can contain CO2, H2O, O2, N2, CO, NO2, and others!
In order to get a better estimate of the performance of the gas turbine, we need to be able to determine the properties of the mixture passing through the turbine

## Slide 7: Nomenclature
In this section, there are a number of subscripts that you need to keep straight. These are:
  m: This is describing the ‘mixture’
  i: Describing an ‘individual’ species (one of the k’s)
  k: Assigns a number to each unique species
Additionally, B or b is a placeholder for any Extensive (B) or Intensive (b) property.
  B could be U (internal energy)
  B could be H (enthalpy)
  b could be h (specific enthalpy)
  b could be v (specific volume)

## Slide 8: Properties of Ideal Gas Mixtures
Consider any property, B (extensive) or b (intensive). For a mixture,
Mass Basis*
mass fraction
Molar Basis
mole fraction**
**Note: The text uses ci for mole fractions
*Other common words: weight basis or gravimetric basis

## Slide 9: Mass/Mole Fraction Conversion
In some instances, a conversion between mass fraction and mole fraction is needed. The mass of a substance is related to the number of moles through the molecular mass, Mi ,
Calculating the mass fraction from known mole fraction:

## Slide 10: Mass/Mole Fraction Conversion
Calculating the mole fraction fro known mass fraction:
Summary of findings ...

## Slide 11: Example
Given: A mixture of ideal gases has the following molar composition; Argon (yAr = 0.20), helium (yHe = 0.54), and the balance is carbon monoxide.
Find: (a) mole fraction of carbon monoxide
(b) the molecular mass of the mixture
(c) the gravimetric (mass) composition of the mixture
Note: The molecular mass of the mixture can be found by,

## Slide 12: Example
The mole fractions of the argon and helium are given. Therefore, the mole fraction of carbon monoxide can be found,
Now, the molecular mass of the mixture can be found,

## Slide 13: Example
The mass fraction composition of the mixture can be found by,
Therefore,

## Slide 14: Example
Comparison of mole fractions and mass fractions for this mixture ...
Component | y | w
Ar | 0.20 | 0.458
He | 0.54 | 0.124
CO | 0.26 | 0.418
1.00
1.00
It is always a good idea to check if the calculated fractions sum up to one!

## Slide 15: Ideal Gas Mixture Properties
We have previously seen that,
Consider the internal energy and enthalpy of an ideal gas mixture. The components of the mixture exist at the same temperature as the mixture. Therefore, according to the expressions above,

## Slide 16: Another Example
Given: A mixture of ideal gases is contained in a closed, rigid container that has a volume of 2 ft3. The mixture is an equimolar binary mixture of methane and ethane. The mixture is initially at 15 psia, 20°F. Heat is now transferred to the mixture pressure and temperature become 60 psia, 300°F.
Find: The amount of heat transferred in this process.