## Slide 1: FEA
Reference Guide
See additional material here

## Slide 2: Setting Up
Make Part or Product
Assign Material Properties
  Ideally done during part creation
  Can be done in Generative Structural Analysis workbench
  Needed for FEA Analysis

## Slide 3: Mesh
Divides up the part to perform analysis
  Can be adjusted by clicking on the symbol
  Can be adjusted by clicking in design tree
  Needed for FEA Analysis

## Slide 4: Mesh
Mesh Size
  The elemental size of part divisions
Mesh Sag
  Max distance between mesh and actual curve

## Slide 5: Mesh
Linear Mesh
  Quick simple mesh
  Good for non critical parts
Parabolic Mesh
  Longer, more accurate mesh
  Good for critical parts
Tetrahedron Elements
linear parabolic

## Slide 6: Analysis Supports
Constraints on existing geometry
Used for FEA Analysis on Products
Based on existing geometry
Can be created in the Assembly Design workbench using the constraints toolbar

## Slide 7: Analysis Supports
General Analysis Connection
Point Analysis
Line Analysis
Surface Analysis
Points to Points Analysis

## Slide 8: Connection Properties
Used to define boundary interactions between bodies
Used for FEA Analysis on Products
Based on existing Analysis Supports or an Assembly Restraint

## Slide 9: Connection Properties
Fastened Connection Property
  Allows two bodies to behave as one
Slider Connection Property
  Allows sliding in tangential planes
Contact Connection Property
  Allows movement until contact is made

## Slide 10: Connection Properties
Fastened Spring Connection Property
  Forms elastic connection between faces
Pressure Fitting Connection Property
  Links two bodies with a negative clearance
Bolt Tightening Connection Property
  Takes into account bolt pre-tensioning

## Slide 11: Connection Properties
Rigid Connection Property
  Links two bodies as infinitely rigid
Smooth Connection Property
  Links two bodies with elastic deformation
Virtual Bolt Tightening Connection Property
  Takes into account virtual bolt pre-tensioning

## Slide 12: Connection Properties
Virtual Spring Bolt Tightening Connection Property
  Takes into account virtual bolt tightening similar to Virtual Bolt Tightening
Customized User-Defined Connection Property
  Allows user to specify elements and the properties associated

## Slide 13: Restraints
Used to restrain a part(s) as the application deems necessary
Used in all applications
Can incorporate virtual parts
Needed for FEA Analysis

## Slide 14: Restraints
Clamp
  Fully restrains a support from moving
User-Defined
  Restrain a support in any combination of X, Y, and Z translation and rotation
Isostatic
  Restrain used for frequency analysis

## Slide 15: Restraints
Surface Slider
Slider
Sliding Pivot
Ball joint
Pivot

## Slide 16: Loads
Model forces acting on part
Not needed in Frequency Analysis
Needed for Static Analysis

## Slide 17: Loads
Distributed Load
Distributed Pressure
Moment
Enforced Displacement
Temperature Field
Mass Density (Frequency)

## Slide 18: Solution
Compute
  Meshes and computes the analysis
Save
  Saves you analysis results
html Report
  Generates an html report of the analysis

## Slide 19: Post Processing
Visualize the results of the FEA analysis

## Slide 20: Post Processing
Deformation
  Shows the deformed part from analysis
Displacement
  Shows the displacement of the part
Von Mises Stress
  Shows the stress distribution of the part

## Slide 21: Post Processing
Animation
  Animates current image from unloaded to loaded states
Scaling
  Scales the image to better see effects
Max/Min
  Finds a minimum or maximum stress value

## Slide 22: Post Processing
Cut Planes
  See a cut out of the analysis results
Principle Stresses
  See Von Mises principle stress state
View Modes
  Shading with edges shows the mesh and results, shading with material does not show mesh