## Slide 1: Testing the effects of support selection and mesh size on analysis.
Geoffrey Wood
Atticus Zborowski
Analysis of FEA Supports and Mesh

## Slide 2: Choosing the wrong support can significantly change the analysis results

## Slide 3: We created a test case to explore methods of constraining a beam
TEST CASE:
3x3x20-in bar
0.5-in mesh size
0.2-in sag
-1,200 lbf in the ‘Z’ direction

## Slide 4: Smaller mesh sizes are better. Or are they…?
Smaller mesh size generally fits to the part geometry better, unless the part is not easily divisible by the mesh size.
We will investigate the effects of changing mesh size of a cantilever beam, measuring error from a hand calculation, and hoping to discover a converging solution.

## Slide 5
DISCOVERIES:
  Choosing incorrect supports can significantly change analysis results
  If a part is changed, even in insignificant ways, the analysis will change because the mesh was generated differently
  CATIA has an error that varies with the size of the mesh, but precision depends on how closely the mesh geometry matches the actual geometry. Smaller mesh is generally better, but not always.