## Slide 1: DELMIA Human and Machine Interaction Simulation
Quallen, Sean
Oster, Adam

## Slide 2: BE WARNED
THIS WILL NOT BE EASY
DELMIA is a product lifecycle management tool
Lifecycles are processes
Therefore everything about DELMIA is a process
Put on your patient hat, and get ready for a long process to get a good product

## Slide 3: First Off
If a human process simulation is all that is needed, then go to the next slide
If a machining simulation is required as well as the human interaction with the process, then the machining process needs to be defined as a catalogued process. We didn’t know this, so no help can be provided. Sorry.

## Slide 4: Now you know what we don’t know
Set Referential point in left heel in the manikin’s properties when initially defining the manikin
Place the manikin in a product with the other products it is going to be interacting with, unless there is machining to be done on a product. Leave that product out, we’ll get back to it later. *You may also want to leave any machines out that are doing machining. It is speculated that they will come with the catalogued process, but we’re not sure. This asterisk will be discussed further at the end in hopes of future work being done with this.

## Slide 5: Before going further
Start DELMIA
Go to Tools->Options
Under the general section, licensing tab, uncheck all licenses
DELMIA will bark, ignore it
Restart DELMIA
Select the EXE2+ and the ACD2+ licenses
Restart DELMIA again
Now the Human Task Simulation workbench is available under the ergonomics design and analysis section

## Slide 6: Next
When defining the process the manikin and the other products need to be resources under the resource list.
If there is machining done to a product to change it, don’t import the product as a resource. Import it under the product list.

## Slide 7: A New Process
Process-The entire simulation of manikin and machine actions
Go to Start->Machining->Advanced Machining.
Right-click on the resource list and go to resource context or insert resource and select the product that includes the manikin and all the stuff the manikin will be using

## Slide 8: Human Task Simulation
With the process open, go to Start ->Ergonomics Design & Analysis ->Human Task Simulation
Use the compass to move all of the products and manikin to the positions you would like them have at the beginning of the process
Once everything is placed properly, click on the save initial position button to save this initial position

## Slide 9: Getting the Womanikin to Move
Click on the rule-based walk button select the manikin as the human resource
The walking speed can be set, or the whole walk can be time-based
Select the floor surface the manikin will be walking on
Leave it as point continuity, and define the path, by clicking the different points
DELMIA will automatically generate the poses of the walk

## Slide 10: Grabbing Objects
There are two steps to grabbing objects:
Reaching for the object
“Picking” the object

## Slide 11: Grabbing Objects (1)
To reach for the object, you can use the “reach” button, to move the manikin from the pose it is in, to the object it is going grab
Alternatively the manikin can be moved to the desired grabbing position using the “Move to Posture” button and the compass

## Slide 12: “Moving to Posture”
Click on the “Move to Posture” button
Move the manikin to the desired position manually
Right-Clicking when moving the manikin will allow for other joint rotations to be achieved if they are allowed
Once the manikin is in the correct position click on the generate posture and DELMIA will simulate all poses to go between the two postures

## Slide 13: Grabbing Objects (2)
Once the manikin has moved to the desired grabbing posture, click on the “pick” button
This will create a logical attachment between the manikin and the product
If the manikin isn’t touching the part when “picking” it, the part will float in space with the manikin when the manikin moves

## Slide 14: Placing Objects
Similar to picking, only placing
Get the manikin into the desired placing position by “reaching” or “moving”
Click the “place” button to remove the logical relation between manikin and product

## Slide 15: Future Development
Define machine operations using the “Create a Machining Process” to see what that yields when used in conjunction with the human simulation
This will not be easy
Catalogs of tools also need to be defined; this catalog may already be underway from other projects, check on this first