## Slide 1: Introduction to 3D Printing

## Slide 2: Basic diagram (Fused Filament Fabrication)
Movement in 3-axis
Raw material (filament)
  Raw material control (extruder)
Surface for manufacturing (bed)
Control system

## Slide 3: 3D printing process

## Slide 4: 3D CAD model
Create 3D models
  Solidworks
  FreeCAD
  Sketchup
  OpenSCAD

## Slide 5: 3D CAD model
Use existing models
  Thingiverse
  Grabcad
  Other sources
Check license

## Slide 6: Slicing software
https://3dprinter.sindoh.com/en/support/downloads

## Slide 7: Design considerations
Print volume (aka "build volume")
Bed adhesion
Layer adhesion
Support material
Print directionality
Feature size
MarkForged Onyx Pro
MarkForged MarkTwo
Sindoh 2X
Sindoh 3DWOX1

## Slide 8: Build Volume
 | 3DWOX1 234F | 2X | OnyxPro / MarkTwo
Build Volume | 210 x 200 x 195 mm | 228 x 200 x300 mm | 320 x 132 x 154 mm
Layer Height | 0.050 - 0.2 mm | 0.050 - 0.2 mm | 0.1 - 0.2 mm
Materials | PLA/ABS (other non-sindoh) | PLA/ABS/TPU/PVA (other non-sindoh) | Onyx/Nylon MarkTwo only: Cont. fiber reinforcement (Carbon Fiber, Fiber Glass, HSHT Fiber Glass, Kevlar)

## Slide 9: Bed Adhesion
Prevent inadvertent separation
Reduce warping
3 types
  Raft – stabilize models with small footprint
  Brim – add stability that's easy to remove
  Skirt – prime nozzle for steady flow

## Slide 10: Layer Adhesion
Affected by:
  Hot end clogs
  Print speed
  Hot end temp
  Filament feed rate
  Part cooling
  Layer height
  Moisture in filament
  Nozzle width

## Slide 11: Effects of Print Directionality
X/Y plane
  High resolution
  High strength
Z/X and Z/Y planes
  Weaker along layer lines

## Slide 12: Support material and Feature Size
Nozzle is 0.4 mm
Can’t reliably make smaller features
  Can make smaller features such as holes with trial and error
Preferable at least 2 x nozzle width (~ > 1 mm)

## Slide 13: How do you print a part?
Make a part in Solidworks
Export part as an STL (using "save-as")
Import (or drag and drop) STL into slicer
Select printer and print material
Adjust print settings or use default ("Normal" from Easy Mode)
Build layers ("Layer Viewer" in 3DWOX Desktop)
File-->Save G-Code to flash drive
Put flash drive into printer usb port
Select "Print", Select your file, and follow on-screen instructions