## Slide 1: Mechanics of Materials Engr 350 - Lecture 8 Mechanical Properties #2

## Slide 2: Hooke’s Law (pronounce like ‘hook’)
The initial portion of the stress-strain curve is linear
𝜎
𝜀
Hooke’s Law gives us the relationship of stress and strain ONLY in the elastic region of the curve
    where E is the modulus of elasticity
Hooke’s Law also applies to shear stress and shear strain
    where G is the modulus of rigidity (also known as the shear modulus)
Hooke’s Law
Hooke’s Law

## Slide 3: Poisson’s ratio (rhymes with ‘boy-john’)
If a solid body is subjected to an axial tension, it contracts in lateral directions
If a solid body is compressed, it expands in lateral directions
Only applies to a state of uniaxial stress
Typical values  1/4 to 1/3
Max value  0.5 (rubber, etc.)
Demonstration?

## Slide 4: Example Philpot 3.4
 within expected values

What has Young’s modulus of ~17 Mpsi?
  Copper red brass alloy

## Slide 5: Another in-class problem
Polymer bar with dimensions:
  b = 50 mm
  d = 100 mm
  h = 270 mm
Load P of 135 kN results in a reduction in height of Δh = -2.50 mm and depth changes by Δd = 0.38 mm
When unloaded the bar returns to original shape. Calculate:
Modulus of Elasticity (Young’s Modulus)
Poisson’s Ratio
Change in dimension b