## Slide 1: Mechanics of Materials Engr 350 - Lecture 9 Design/Safety
“Design is a funny word. Some people think design means how it looks. But of course, if you dig deeper, it's really how it works.”
-Steve Jobs

## Slide 2: Design considerations
We generally must make many assumptions in design in order to make calculations.
4 Types of Loads
  Dead Loads
  Live Loads
  Snow Loads
  Wind Loads

## Slide 3: Design approaches - Allowable Stress Design (ASD)
Component is designed so that elastic stresses do not exceed a percentage of the yield strength
Usually accomplished by applying a factor of safety.
where σfailure may be σultimate or σyield
FS:
~2.0 for buildings
~3.5-4.0 for pressure vessels
~3.0 for automobiles
~1.5 aerospace (but frequent inspections)
~4-10 loss of life failures
𝜎
𝜀
115ksi
𝜎allow= 76.7ksi
0.2%

## Slide 4: Example

## Slide 5: Design approaches - Load And Resistance Factor (LRFD)
Probabilistic design concept - Uses statistical probabilities to optimize risk of failure
Chain hook example

## Slide 6: Statistics Background Frequency Distribution Plot (histogram)
Mean of data set
Frequency
(# times data observed)
The whole data set (many replicates)

## Slide 7: Load and Resistance Factor - LRFD cont.
Strength data from testing many different hooks off the production line.
Measure forces (or stress/strain) in hooks as used by customers
Resistance (R*)
Strength of the part in question
Load Effects (Q*)
Effect of observed loads on the part in question

## Slide 8: LRFD cont.
Plot the actual strengths (resistance) and the actual loads together
Can shift the position of these distributions with the load factor (𝛾), and the resistance factor (𝜙)
In general we want
𝜙Rn>𝛾Q1+𝛾Q2+….+𝛾Qn
Resistance (R*)
Load Effect (Q*)
Overlap = Failure!!!
Probability of Failure

## Slide 9: LRFD cont.
Common Load and Resistance Factors
𝜙Rn>𝛾Q1+𝛾Q2+….+𝛾Qn
Load Factors (usually > 1)
            Dead Loads  γ = 1.2
      Live Loads  γ = 1.6
  = 0.001 is the notional failure rate (higher than actual, considered safe)
  = 0.001 means 1 in 1000 chance of failure
Resistance Factor (R*)
Load Effect (Q*)
Resistance Factors (often < 1)
            Depends on likelihood of simultaneous conditions
            ϕ = 1, simultaneous conditions likely
            ϕ < 1, simultaneous conditions less likely
            For instance, high snow load *and* high wind load unlikely

## Slide 10: Example 4.3 – Compare ASD to LRFD

## Slide 11: Example 4.3 – Compare ASD to LRFD