## Slide 1: Lecture 3
Thermodynamic Concepts

## Slide 2: Terminology
System
  Whatever is being studied
System boundary
  Imaginary boundary that separates the system from its surroundings
  A control volume is one example (non-moving)
Three Classifications:
  Open system
    Mass and/or energy can be transferred across the system boundary
  Closed system
    No transfer of mass across the system boundary
    Energy can cross the system boundary
  Isolated system
    No transfer of mass or energy across the system boundary

## Slide 3: Engine Example #1
System
  Gas in the cylinder
System boundary
  Changes volume as the piston moves up and down
Closed system
  Only energy crosses the boundary during compression, combustion, and expansion
Open system
  Both mass and energy cross the boundary (during intake and exhaust processes)
Piston-cylinder assembly in an internal combustion engine
Valve
Spark plug
Valve

## Slide 4: Engine Example #2
System
  What is the system being studied?
System boundary
  Is it fixed or moveable?
System type
  Is the system isolated, open, or closed?
An internal combustion engine

## Slide 5: System Descriptions
Microscopic view
  Considers atomic and molecular contributions to properties of substances
  Important when dealing on micro and nano scales
Macroscopic view (continuum thermodynamics)
  Considers only bulk behavior of a substance
  Molecular size and time scales much smaller than problem being analyzed
  Point of view used in ME 322!

## Slide 6: Properties
A property is a characteristic of a system
Intensive Properties
  Independent of mass
    Examples: pressure, temperature
Extensive Properties
  Dependent on mass
    Examples: Mass, total volume
Intensive/Extensive Cut-Test
  Cut a volume of substance in half
    If the property of the half is the same as the whole, then the property is intensive

## Slide 7: Notation
Intensive properties – signified with a lower case letter. Intensive properties are usually preceded with the word ‘specific’. Exception: T (temperature)
Extensive properties – signified with a upper case letter. Exceptions: m (mass), n (moles)
Table 2.1 lists specific kinetic and specific potential energy. Are these properties?

## Slide 8: Thermodynamic State
This is known as the State Postulate for simple systems
What is a pure substance? (more details on next slide)
What is a work mode?
What is a homogeneous substance? (more details on next slide)
When are intensive properties independent?
When are intensive properties dependent?

## Slide 9: Pure Substances vs. Mixtures

## Slide 10: Properties, States, and Processes
Pressure
(property)
Temperature
(property)
(State 1)
(State 2)
Process – a series of states that occur as a system’s state is changed from state 1 to state 2
Consider a single phase pure substance (simple substance)

## Slide 11: Equilibrium
From mechanics
  Equilibrium is defined as a condition of balanced forces
Thermodynamic equilibrium
  Balance of several influences simultaneously
    Forces and pressure (mechanical)
    Temperature (thermal)
    Chemical composition (chemical)
    Others (phase, magnetic, etc.)

## Slide 12: Pressure and Temperature
Pressure = force per unit area
Common units = lbf/in2 (psi) or N/m2 (Pa)
Temperature = a measure of molecular activity in a substance
Conversions
Notice …

## Slide 13: Absolute and Relative Values
In ME 322 pressure is most often expressed on the absolute scale. Temperature can be either relative or absolute. Recall that 1 atm = 14.696 psi = 101325 Pa (or 101.325 kPa).

## Slide 14: When to use Absolute Values?
If pressure or temperature stands by itself, or is raised to some power in an equation, then the values assigned to it must be in an absolute scale of units!
For example, in the ideal gas equation p = mRT, both the pressure and temperature stand alone, so they both must be in absolute units. However, for the case of a constant volume and constant mass system, we can write this equation as:
(p2 – p1)V = mR(T2 – T1)
and since this equation has pressure and temperature differences, then they can both be in either absolute or relative units.

## Slide 15: The Zeroth Law of Thermodynamics
Standard Thermometer
Fixed Points
(e.g., freezing point of zinc)
692.677 K 419.527°C
If TA = TB and TB = TC, then TA = TC
TC
Calibrated Thermometer
TA
TB
Calibration using the Standard
TB

## Slide 16: Transitive Laws
TA = TB and TB = TC  then TA = TC
The above is an example of a transitive law. Many (but not all) properties have this relationship. For instance, here is an example of something that doesn’t obey the transitive law
Sandy loves Kevin S = K
Kevin loves his mom, Gertrud K = G
Sandy does *not* love Gertrud S ≠ G