## Slide 1: Lecture 28b
Comparing Internal Combustion Engines
Gasoline (Spark Ignition – SI)
Diesel (Compression Ignition – CI)

## Slide 2: Comparing SI and CI
Mean Effective Pressure
Cycle Thermal Efficiency
CI, FI ~1400-2000 kPa (200-300 psia) CI, NA ~700-900 kPa | SI, FI ~1200-1700 kPa (175-250 psia) SI, NA ~850-1200 kPa
Which cycle has higher thermal efficiency?

## Slide 3: Comparing SI and CI

## Slide 4: Supercharger vs. Turbocharger
Supercharger
Both increase pressure in the intake manifold
Supercharger can be positive displacement or centrifugal
Turbocharger uses centrifugal compressor
Turbocharger

## Slide 5: Supercharger vs. Turbocharger
Supercharger
1, 8
2
3
4
BDC
TDC
5
6
7
1, 8
2
3
4
BDC
TDC
5
6
7
Power for the compressor comes from:
Supercharger  driven by crankshaft
Turbocharger  driven by turbine in exhaust
Turbocharger

## Slide 6: SI Engine – Forced Induction
Add Processes to P-v Diagram:
Exhaust process (slightly above atmospheric pressure)
Intake process (boost pressure above atmospheric pressure)
Clockwise power cycle  Positive Work
Clockwise exhaust/intake cycle  Positive Work!
Practical Considerations:
Compressing a mixture of air and fuel
Must stay below the autoignition pressure and temperature
For high-boost engines (above ~10 psi boost), CR is reduced
1, 8
2
3
4
BDC
TDC
5
6
7

## Slide 7: CI Engine – Forced Induction
Add Processes to P-v Diagram:
Exhaust process (slightly above atmospheric pressure)
Intake process (high higher than atmospheric pressure)
Clockwise power cycle  Positive Work
Clockwise exhaust/intake cycle  Positive Work!
Practical Considerations:
Compressing air only
No danger of autoignition
More boost = more positive work during intake stroke!
Primary limitation is peak in-cylinder pressure during combustion
1, 8
2
BDC
TDC
5
6
7
3
4

## Slide 8: Blurring The Lines
Modern gasoline engines are experimenting with:
Direct-Injection
  Fuel is injected directly in the cylinder, though still before TDC
  Mixture is ignited with spark plugs
  Can create stratified charge (regions of stoichiometric air-fuel mixture, and regions of air without fuel)
Throttless Load Control
  Reduce pumping losses at part-load (cruise) by eliminating the throttle
    Diluting the incoming air with exhaust gases
    Closing intake valve early (or very late)
    Cylinder deactivation (running fewer cylinders at full load)

## Slide 9: Blurring The Lines
Modern diesel engines are experimenting with:
Homogeneous Charge Compression Ignition (HCCI)
  Fuel is pre-mixed with air before compression stroke
  TDC autoignition results in nearly instantaneous combustion
  Control is very difficult, but promises cycle efficiency near ideal Otto cycle
Common-Rail Fuel Injection
  Electronic control of fuel injectors
  Split firing (pre-fuel, then main fuel)
Variable Nr Engines
  With discrete valve control it is possible to switch a 4-stroke engine to be a 6-stroke, 8-stroke, 10-stroke, etc. engine.
  The lighter the load the more power strokes could be had before exchanging the exhaust with fresh air.