Analysis of Total PCB Content by Reductive Dechlorination to Biphenyl

John G. Doyle, TeriAnn Miles, Erik Parker,

# I. Francis Cheng

Department of Chemistry

University of Idaho

Moscow, Idaho 83844-2343

ifcheng@uidaho.edu

(208) 885-6387

Outline

- Short History of PCBs

- Present state of PCB analysis

Multi-component – 209 congeners

Associated problems with GC-ECD

- Chemical Reaction to Single Species

Carbon Skeleton

Perchlorination

- Complete dechlorination at RTP.

Pd/Mg bimetallic particles

Performance with Arochlor( 1221

- Elimination of Interferences by other Halocarbons

Mixtures of DDT and Arochlor 1260

PCB history

10 ( x + y

# Industrial uses 1930 – 1977

- Dielectric fluids, capacitors and transformers

- Printing inks

- Paints

- Pesticides

# Health and Environmental Risks

- Occupational exposure (1936)

- Bio-accumulative (low water solubility)

- Banned by TSCA 1977

# EPA policy

Soils: nonrestricted access areas must 10 ppm or less

PCB analyses

209 possible congeners

GC-FID of a PCB mixture

## Complicating Features

CG-ECD analysis based on pattern recognition of key congener peaks.

- Matrix effects

-DDT/DDE metabolites

-Other Halocarbons

- Environmental aging

-Different rates of dechlorination for each

congener

-Volatility differences for each congener

- ECD response

-Varies with each congener

“Sources and Magnitude of Bias Associated with Determination of Polychlorinated Biphenyls in Environmental Samples” Analytical Chemistry, 1991, 63, 2130-2137.

Chemical Reaction of PCBs

To one predominate species

1. Reductive Dechlorination:

2. Perchlorination:

Requirements for Chemical Reaction to Single Species

- Reproducible and Quantitative

100% Yield

- Rapid

Room Temperature and Pressure

3.Simple

minimal work-up

## Literature methods

Reductive Dechlorination:

| Procedure | Analysis | Detection Limit |
| --- | --- | --- |
| H2 reduction on Pd catalyst @ 3050C | GC-FID | 150 ng |
| Heated Pd catalysts | GC-FID | 10 ng |
| Na reduction | Cl- ISE | 10 mg |
| LiAlH4 | HPLC UV@248 nm | 100 ng |

Perchlorination

| SbCl5 @ 2050C | GC-ECD | ? |
| --- | --- | --- |

Most of the above involve extensive procedures.

Rapid reductive dechlorination under mild conditions

1. Standard Reduction Potential of PCBs

E0red = 0.5 to 1.0 volts

## Reducing Agents (aqueous)

## E0red

## Fe ( Fe2+ + 2e-				-0.44 V

Cr ( Cr3+ + 3e-				-0.74 V

Mn ( Mn2+ + 2e-				-1.182 V

Mg ( Mg2+ + 2e-				-2.36 V

Complete dechlorination of PCB by zero-valent metals is slow.

- Most congeners are completely stable in presence of metal reducing agents at RTP.

- Requires catalyst.

Pd/Fe bimetallic system*.

- 2 g, 10 (m, 99.9% Fe particles

- 0.05 % Pd w/w

- 5 ml 20 ppm Arochlor 1260

(30% MeOH , 20% acetone, 50% water)

- Complete dechlorination in 10 minutes

- Majority product, biphenyl

*C. Grittini, M. Malcomson, Q. Fernando, N. Korte

Environ. Sci. & Tech., 1995, 29, 2898-2900.

Analysis of total PCB by reductive dechlorination with Pd/Mg bimetal.

- Mg vs. Fe

- Fe surface requires extensive pretreatment

- Anaerobic acid washing

- Air sensitive

- Mg requires no special treatment

- Deposition of Pd onto Mg

- Untreated 0.5 grams 20 mesh Mg

- (98%, Aldrich)

- 20 mg K2PdCl6

PdCl62- + 2Mg = Pd + 6Cl- + 2Mg2+

PCB dechlorination

Analyte solution

- 3-5 ml of 50/50 v/v 2-propanol/water

- 1 – 60 (M Arochlor 1221

- 0.5 grams 20 mesh Mg particles

- 20 mg K2PdCl6 powder

- reaction complete in 5 minutes

Preparation for HPLC

- syringe filter 0.2 ml of above

Role of Pd in the catalysis of zero-valent metal reduction of halocarbons.

- Pd is a catalytic surface for hydrogen evolution

- Increases Mg dissolution (galvanic corrosion)

- Hydrogen intercalates in bulk Pd

- May result in excellent surface for hydrodehalogenation

- Pt fails as hydrodehalogenation catalyst

I.F. Cheng, Q. Fernando, N. Korte, Environmental Science and Technology, 1997, 31(4) 1074-1078.

Analytical performance of Mg/Pd reductive dechlorination system

### HPLC analysis

### 50 uL sampling loop

### UV absorbance detector 200 nm (HP 79853C)

### Isocratic 65/35 v/v acetonitrile/water

### C-8 Zorbax column

Arochlor 1221 biphenyl content, 3.3%

### Biphenyl Calibration Curve

## Biphenyl from Arochlor 1221 dechlorination

## Biphenyl yield = 98% (from slopes)

Chemical Interferences

## DDT and major impurities and metabolites

- 10 major GC-FID peaks

- Co-elute with PCBs

Reductive dechlorination of DDT/metabolites by Pd/Mg.

- RTP reaction completed in 10 minutes

- Only demonstrated method for the complete and rapid dechlorination of DDT at RTP

Procedure as with PCB dechlorination

GC-FID of PCB & DDT mixtures

## Illustrates DDT interference

Top 50 ppm PCB (Arochlor 1260) and 50 ppm DDT

Bottom 50 ppm DDT

Pd/Mg Treatment of DDT/PCB mixtures

GC-FID

- Conclusions and Future Work

# Advantages

## PCB reductive dechlorination by Pd/Mg to biphenyl

- Rapid (< 5mins)

- Reproducible (98% yield)

- Detection Limit (no sample preconcentration)

5 x 10-6M

100 ppb

5 ng

# Disadvantages

- Loss of congener specific information

- Requires analysis for biphenyl background

# Future

- Elimination of halocarbon interferences (DDT)

Acknowledgements

# Co-authors

John G. Doyle

TeriAnn Miles

Erik Parker

# Other Contributors

Mark Engelmann

Kristy Henscheid

Keri Colvin

Roshan Koshravi

Josh Linard

University of Idaho Research start-up funds

Contact Information:

Frank Cheng

Department of Chemistry

University of Idaho

Moscow, Idaho 83844-2343

ifcheng@uidaho.edu

(208) 885-6387

# Text boxes

Major product of DDT/metabolite reductive dechlorination