## Slide 1: Selective Electrochemical Detection of Triacetone Triperoxide
Yuqun Xie
Chemistry Department of University of Idaho

## Slide 2: Outline
Background
  Synthesis
  Dangers
Detection
  Current state of detection
  Urgent needs for TATP detection
Proposed method
Results
Conclusion
Acknowledgement

## Slide 3: Triacetone Triperoxide (TATP)
Chemical formula: C9H18O6
TATP is highly unstable explosive. Susceptible to heat, friction, and shock.
http://en.wikipedia.org/wiki/Acetone_peroxide

## Slide 4: TATP Synthesis
3H2O2 + 3CH3COCH3 ((CH3)2COO)3 + 3H2O
H+
< 10°C
All the reactants are commercially available:
Acetone (hardware stores paint thinner)
Hydrogen peroxide (pharmacies)
sulfuric acid (Battery acid)
Widmer, Leo; Watson, Stuart; Schlatter, Konrad; Crowson, Andrew. Analyst 2002, 127, 1627-1632.
Dubnikova, Faina; et al J. Am. Chem. Soc. 2005, 127, 1146-1159.

## Slide 5: Hexamethylenetriperoxide (HMTD)
HMTD
http://en.wikipedia.org/wiki/Hexamethylene_triperoxide_diamine
Oxley, J.C.; Smith, J.L.; Chen, H.; Cioffi, Eugene. Thermochim. Acta 2002, 388, 215-225
Hexamethylenetetramine + Citric Acid + H2O2 HMTD
< 10°C
http://business.fortunecity.com/executive/674/hmtd.html
Hexamethylenetetramine fire starter

## Slide 6: TATP &HMTD Incidents
2007 - German authorities stop terrorist plot and seize 1500 lbs of H2O2.
2006 - London airline bombing plot – HMTD
2005 - Joel Henry Hinrichs III – University of Oklahoma. – TATP.
2001 - Richard Reid, Shoe Bomber – TATP
1999 - Millennium bomber Ahmed Ressam. 124 pounds of HMTD
1994/95 – Bojinka Plot – TATP? HMTD?
1994 – Philippines Airlines - TATP
1980’s – present - West Bank Israel – TATP “Mother of Satan”

## Slide 7: TATP – TSA Fluid Ban
Effective November 10, 2006, the TSA has advised that travelers may now carry through security checkpoints travel-size toiletries (3.4 ounces/100 ml or less) that fit comfortably in ONE, QUART-SIZE, clear plastic re-sealable bag.
  The 3-1-1 Kit contains six 2-1/2 oz and four 1-1/2 oz flexible squeeze tubes, plus one 1-3/4 oz Envirosprayer.
  Kit is also compliant with the new International Security Measures Accord.
  http://www.easytravelerinc.com/

## Slide 8: Current techniques for TATP detection
IR-Raman
  High Selectivity – Relatively High LOD
Fluorescence/UV-vis Absorbance
  Low LOD requires tagging
Ion Mobility
  Good Selectivity, moderate LOD
HPLC or GC
  Excellent Selectivity and LOD
Enzymatic
  Moderate LOD requires pretreatments
Derek F. Laine, I. Francis Cheng . Microchemical Journal 91 (2009) 125–128.
Wang, Joseph et al, Analyst 2007, 132, 560-565.

## Slide 9: Disadvantages of Present TATP Detector Designs
Interferences ( O2 and/or other peroxides)
Time consuming (several minutes)
Expensive
Non-portable

## Slide 10: Urgent needs for TATP Detection
Small Portable
  hand hold sensor or test strip
Highly selective
  distinguishing TATP from organic peroxide interference
Fast
  less than 30 s
Cheap
  costs few dollars
Easy to use
  users don’t need be trained
Low detection limits
  Micro Molar

## Slide 11: Reference Reaction
Mair, R.D.; Graupner A.J., “Determination of Organic Peroxides by iodine Liberation Procedures” Analytical Chemistry, 1964, 26, 194-204.
Chemical Reaction
Need be purged with N2 due to the O2 interference

## Slide 12: Proposed method
TATP+ 4Br- + 2H+ 2C3H5OBr+ C3H4Br2 +3H2O
HMTD+2Br- + H+ Br2+ fragments
H2O2 +2Br- + 2H+ Br2 +2 H2O
Electrode reaction:
Fast (less than 30 s)
Slight temperature elevation (550C)
No interference from O2
Chemical Reaction:
Br2 + 2e- 2Br- Estep = 0.70 volts vs. Ag/AgCl
2Br-  Br2 + 2e- Estep = 0.96 volts vs. Ag/AgCl

## Slide 13: Detection Scheme
Amperometric detection of peroxides
  Absence of aqueous Br2 - TATP
  Appearance of aqueous Br2 - HMTD, H2O2 & other peroxides

## Slide 14: Cyclic voltammetry of Redox couple Br-/Br2
Chart: 
Br2 + 2e- 2Br- Estep = 0.70 volts vs. Ag/AgCl
2Br-  Br2 + 2e- Estep = 0.96 volts vs. Ag/AgCl
Cyclic voltammograms , 11.94 M Acetic acid, 0.364 m M HCl. sweep rate is 30 mV/s.
a) 0 mMKBr
b) 3 mM KBr.

## Slide 15: Chronoamperometry (CA), TATP
Chart: 
Double step Chronoamperometry 11.94 M Acetic acid, 0.364 m M HCl , 0.3 m M KBr and various concentration of TATP . Sampling at 5 to 10 s and 15 to 20 s for the calibration curve

## Slide 16: Calibration curve of TATP based on the disappearing the Br- and absence of Br2 correspond to the CA
Chart: TATP Concentration (µM)
| 0 | 25 | 50 | 62.5 | 75 | 100
960 mV | -5.6008 | -4.9565 | -4.0902 | -3.6666 | -3.3395 | -2.5637
700 mV | -1.2195 | -1.2195 | -1.2195 | -1.2195 | -1.2195 | -1.2195
LOD ( 3 times standard deviation n=3) of TATP is 8.5 µM

## Slide 17: Chronoamperometry (CA), HMTD & H2O2
Chart: 
Double step Chronoamperometry 11.94 M Acetic acid, 0.364 m M HCl ,
6 m M KBr and various concentration of HMTD and H2O2
Chart: 

## Slide 18: Calibration curve of HMTD and H2O2 based on the appearance of Br2 and disappearing of the Br- correspond to the CA
Chart: HMTD Concentration (mM)
| 0 | 0.1 | 0.30000000000000032 | 0.60000000000000064 | 1.2
700 mV | -2.1995 | 1.4732 | 8.9431 | 16.296 | 32.4563
960 mV | -65.1688 | -60.7935 | -55.3165 | -46.0965 | -36.3389
LOD (3 times standard deviation n=3) of HMTD is 16.3 µM, H2O2 is 14.9 µM
Chart: H2O2 Concentration (mM )
| 0 | 0.5 | 1 | 1.5 | 2 | 3 | 4
700 mV | -0.18914 | 2.3765 | 5.0279 | 9.3711 | 11.432 | 18.4564 | 22.6448
960 mV | -42.9638 | -42.0961 | -39.5044 | -36.5544 | -32.7437 | -28.6564 | -26.2749

## Slide 19: Literature Summary
Technique | Pre-treatment | Time (min) | Limit of Detection | Chemical Interferences | Portable (instrument)
This work | No | < 0.5 | 8.51 μM | None | Yes
Electro-catalytic Fenton Reaction | Strong Acid | 10 | 1 μM | Yes | Yes
HRP Colorimetric | UV | 1 | 1 mM | Yes | No
HRP Fluorescence | UV | 30 | 8 μM | Yes | No
HPLC Fluorescence | UV | 15 | 2 μM | Yes | No
GC/MS | SPME | 20 | 5 ng | No | No
IMS | sampling | 50 | 3 mg/m3 | Yes | Yes
Amperometry – Prussian Blue Modified Electrode | UV/laser | 5 | 50nM | Yes | Yes
 | Strong Acid | >1 | 55 nM | Yes | Yes
 | Strong Acid | 1 | 18 mM | Yes | Yes

## Slide 20: Conclusion
Advantages of TATP detection
Highly selective
Non-interference
Low cost
Portable (potential)
Fast ( under 30 s)

## Slide 21: Goal
Fast
Selective
Portable
Cheap
Easy to use
Low detection limits
Glucose sensor
https://www.freestylelite.com

## Slide 22: Acknowledgments
Dr. I. Frank Cheng
Simon McAllister
Kenichi Shimizu
University of Idaho Department of Chemistry; faculty, staff and students.
Dr. and Mrs. Renfrew for summer scholar fund