## Slide 1: ME 345 Heat Transfer (HTx)
Professor:
Dr. Dan Cordon (AKA Dr. Dan)

## Slide 2
Draw the thermal circuit
Use appropriate equation for thermal resistance
  Geometry
  Conduction/Convection/Radiation
Identify which variables are known and unknown
Choose your solution approach (calculator and hand calculations vs. software)
Solving Thermal Resistance Problems

## Slide 3
A 4mm thick front window of a car is defrosted by passing warm (dry) air over the inner surface.
If the inside air is 40 [°C] with convection coefficient of 30 [W/m2K] and the outside air is -10 [°C] with convection coefficient of 65 [W/m2K] – calculate the inside and outside surface temperature of the glass
Is this enough to keep ice from forming on the outside of the glass?
Textbook Problem 3.3

## Slide 4
Assumptions:
1D SS conduction through the window
Material properties not changing with temperature
Radiation HTx is negligible
Textbook Problem 3.3
Known

## Slide 5
Use equations 3.11 and 3.12
Look up thermal conductivity for glass Table A-3, glass at 300 [K], k = 1.4 [W/m-K]
Heat flux (because area unknown) can be expressed by:
Textbook Problem 3.3

## Slide 6
With known heat flux, can evaluate temperature drop across each resistance
At the inner surface
At the outer surface
Textbook Problem 3.3

## Slide 7
Similar problem as 3.3, except now a film heater is applied to inside surface of the window.
If the inside air is 25 [°C] with convection coefficient of 10 [W/m2K] and the outside air is -10 [°C] with convection coefficient of 65 [W/m2K]. Want to maintain inner glass temperature of 15 [°C].
Calculate the heater power required per unit area
Textbook Problem 3.4

## Slide 8
Assumptions:
1D SS conduction through the window
Material properties not changing with temperature
Radiation HTx is negligible
Film heater is thin and highly-conductive (negligible thermal resistance)
Textbook Problem 3.4

## Slide 9
Energy balance (flux) at the inner surface of the window
Solving for heater heat flux:
Textbook Problem 3.4

## Slide 10
Thermopane window on a house is made of two pieces of 7 [mm] thick glass with a 7 [mm] thick air space between them.
The inside and outside temperatures are 20 [°C] and -10 [°C]. The interior convection coefficient is 10 [W/m2K], while the outer is 80 [W/m2K].
Calculate the heat loss rate through a window that is 0.8 [m] tall and 0.5 [m] wide.
Repeat for a triple pane style window
Textbook Problem 3.12

## Slide 11
Assumptions:
1D SS conduction through the window
Material properties not changing with temperature
Radiation HTx is negligible
Air in gap is stagnant
Textbook Problem 3.12
Known

## Slide 12
Use equations 3.11 and 3.12
Look up thermal conductivities Table A-3, glass at 300 [K], k = 1.4 [W/m-K]
Table A-4, air at 278 [K], k = 0.0245 [W/m-K]
Textbook Problem 3.12

## Slide 13
For the triple pane, total thermal resistance increases to 1.749 [K/W], and the heat loss drops to 17.2 [W]
Textbook Problem 3.12

## Slide 14
Firefighter protective turnout coat is typically made of three layers with air gap between each layer. Create the thermal circuit for this boat.
Note: Since radiation heat transfer is significant, include these terms in your thermal circuit.
Textbook Problem 3.24

## Slide 15
Textbook Problem 3.24

## Slide 16
Some interesting approximations for the radiation thermal resistance
This was used to make the calculations easier, and comes from assuming epsilon = 1 (worst-case that would represent maximum heat transferred through radiation)
The radiation thermal resistance can be modeled as
Textbook Problem 3.24

## Slide 17
A cylindrical water heater (100 gallon) uses urethane foam insulation around the outside. The water inside is 55 [°C] and the air temperature outside the heater is 20 [°C]. The convection coefficient between the air and tank is 2 [W/m2K] (low because it is only from natural convection).
If electrical power costs $0.18 / kW-hr, specify dimensions for both the tank *and* insulation so that the annual cost of heat loss from the heater is less than $50.
Textbook Problem 3.46

## Slide 18
Assumptions:
1D SS conduction
Inner surface temperature is nearly the same as water temperature (metal tank)
Neglect radiation (foil covering on insulation)
Constant properties
Textbook Problem 3.46

## Slide 19
Look up thermal conductivity Table A-3, urethane foam at 300 [K], k = 0.026 [W/m-K]
To minimize heat loss we should minimize the surface area.
When the height is defined by:
Surface area of the cylinder is:

Textbook Problem 3.46

## Slide 20
Minimize Asur by taking derivative with respect to diameter and setting equal to zero
We get
Since the tank is 100 gallons = 0.379 m3 we get:
D = L = 0.784 [m]
Textbook Problem 3.46

## Slide 21
Now that we have the dimensions we need to calculate the maximum allowable heat rate
Textbook Problem 3.46

## Slide 22
BIG 1D SS THERMAL RESISTANCE SUMMARY

## Slide 23
Heat loss through the side and ends is
Textbook Problem 3.46
Cylinder wall
Round ends
Conduction
Conduction
Convection
Convection

## Slide 24
Solve for delta (insulation thickness) to get
Textbook Problem 3.46

## Slide 25
Real-world reality check
Water heaters are almost never built with L = D (stress analysis dictates this). Looking up some common dimensions for a 100 gallon water heater
D ~ 0.623 [m], and L ~ 1.245 [m]
Using same thickness for insulation and solving for rate of heat loss we get:
q = 34 [W], and Annual Cost = $53.62
Textbook Problem 3.46

## Slide 26
Are you bored? Run this same calculation for a spherical water heater.
Benefit: Lower surface to volume ratio
Any downsides?
Textbook Problem 3.46