## Slide 1: ME 433 Internal Combustion Engines Review Session #2
Professor:
Dr. Dan Cordon (AKA Dr. Dan)

## Slide 2
Hydrocarbon Fuels (quick overview)
Most common hydrocarbon fuels are Alkyl Compounds and are grouped as:
Paraffins (alkanes): single-bonded, open-chain, saturated
CnH2n+2 n= 1 CH4 methane
n= 2 C2H6 ethane
n= 3 C3H8 propane
n= 4 C4H10 butane
n= 8 C8H18 n-octane and isooctane
C
H
H
H
C
H
H
H
H
C
H
H
C
H
H
C
H
H
C
H
H
C
H
H
C
H
C
H
H
H
H
C
H
H
C
H
H
methane
propane
n-octane
H
H
H
C
H
There are multiple isooctanes, depending on position of methyl (CH3) branches which replace hydrogen atoms (eg. 3 H are replaced with 3 CH3)

## Slide 3
Olefins (alkenes): open-chain containing one double-bond, unsaturated (break bond more hydrogen can be added)
CnH2n n=2 C2H4 ethene
n=3 C3H6 propene
propene
Acetylenes (alkynes): open-chain containing one C-C triple-bond unsaturated
CnH2n-2 n=2 C2H2 acetylene
n=3 C3H4 propyne
H
C
C
H
acetylene
Hydrocarbon Fuels (cont’d)
For alcohols one hydroxyl (OH) group is substituted for one hydrogen
e.g. methane becomes methyl alcohol (CH3OH) or methanol
ethane becomes ethyl alcohol (C2H5OH) or ethanol
H
C
H
H
C
C
H
H
H

## Slide 4
Atom Balancing
If sufficient oxygen is available, a hydrocarbon fuel can be completely
oxidized, the carbon is converted to carbon dioxide (CO2) and the hydrogen is
converted to water (H2O).
The overall chemical equation for the complete combustion of one mole of
propane (C3H8) is:
Elements cannot be created or destroyed so
carbon balance gives b= 3
hydrogen balance gives 2c= 8  c= 4
oxygen balance gives 2b + c = 2a  a= 5
Thus the above reaction is:
# of moles
species

## Slide 5
Generalized Atom Balancing
Air contains molecular nitrogen N2, when the products are low temperature the nitrogen is not significantly affected by the reaction, it is considered inert.
The complete reaction of a general hydrocarbon CaHb with air is:
The above equation defines the stoichiometric proportions of fuel and air.
Example: For propane (C3H8) a= 3 and b= 8

## Slide 6
Generalized A/F Ratio Determination
Substituting the respective molecular weights and dividing top and bottom
by a one gets the following expression that only depends on the ratio of the
number of hydrogen atoms to hydrogen atoms (b/a) in the fuel.
Note above equation only applies to stoichiometric mixtures
For methane (CH4), b/a = 4  (A/F)s = 17.2
For propane (C3H8), b/a = 2.67  (A/F)s = 15.6
The air/fuel and fuel/air ratio on a mass basis is:

## Slide 7: Combustion
Oxidant
The oxidant must contain oxygen. The most abundant ‘free’ source is atmospheric air. By molar percent, atmospheric air is considered to be ...
Chart: 
| Nitrogen | Oxygen
East | 79 | 21
For every mole of oxygen involved in a combustion reaction, there are 79/21 = 3.76 moles of nitrogen.

## Slide 8: Combustion with Air
Air as Oxidizer
1 mole of air is comprised of :
  ~0.21 mole of Oxygen
  ~0.79 mole of Nitrogen
For balancing chemical equations we often write air as:
1 O2 + 3.76 N2
Be careful as the above is not 1 mole of air.
The above represents 4.76 moles of air.
This is especially important when
Calculating molar AFR
Chart: 
| Nitrogen | Oxygen
East | 79 | 21

## Slide 9: Combustion
Products (for fuels with no sulfur content)
- Complete Combustion: CO2, H2O, and N2
- Incomplete Combustion: CO2, H2O, N2, CO, NOx
- Combustion with Excess Oxygen: CO2, H2O, N2, and O2
NOTE: Fuels containing sulfur have the potential of introducing sulfuric acid into the product stream.

## Slide 10: Combustion Terminology
Theoretical Air, or Stoichiometric Mixture
The amount of air required for complete combustion of the fuel
  No air or fuel left over at end of reaction
  Determined by balancing the combustion reaction
Percent Theoretical Air (PTA)
The amount of air actually used in the combustion process relative to the stoichiometric value
  Rich: Incomplete combustion if PTA < 1 (100%)
  Lean: Unconsumed oxygen if PTA > 1 (100%)
Percent Excess Air
The percent of additional air beyond 100% theoretical air
  Only applies to lean mixtures (excess oxidizer)

## Slide 11: Combustion Terminology
In many combustion processes, one of the parameters we are interested in is how much air (or oxygen) is required per unit quantity (moles or mass) of fuel.
Air-Fuel Ratio (AFR) Fuel-Air Ratios

## Slide 12: Combustion Terminology
Dimensionless AFR: Want a way to describe if a mixture is stoichiometric, rich, or lean.
Equivalence Ratio (combustion engineers)
< 1 is lean
= 1 is stoichiometric > 1 is rich

## Slide 13: Combustion Terminology
Dimensionless AFR: Want a way to describe if a mixture is stoichiometric, rich, or lean.
Lambda (engine calibration, mechanics)
< 1 is rich
= 1 is stoichiometric > 1 is lean

## Slide 14: Stoichiometric (Complete) Combustion
5 equations
5 unknowns
(n0 through n4)
Atomic Balance Equations
Stoichiometric Combustion of a General Fuel in Air
Looks like 1 equation and 5 unknowns

## Slide 15: Lean Combustion
PTA = Percent Theoretical Air
expressed as a decimal
6 equations
6 unknowns
(x0 through x5)
Requires a stoichiometric
balance first (to get n0)
Lean Combustion of a General Fuel in Excess Air