Typical Values for Engine Parameters

Parameter			      SI Engines		CI Engines

Air/Fuel Ratio			15:1			20:1 - 70:1

Compression Ratio 	         8:1 -10:1	          15:1-22:1
                                              H.P. up to 13:1

Maximum Speed		      5000-10000 rpm	2000-4000 rpm

Bore/Stroke Ratio		.8-1.2			    .8-1.2

Mean Piston Speed		15-20 m/s		   8 m/s (low speed)
(at maximum power)           H.P. up to 25 m/s        11 m/s (medium speed)
        								 16 m/s (high speed)

Brake Mean Effective	  N.A. 850-1200 kPa	N.A. 700-900 kPa

Pressure, (bmep)		  T.C. 1200-1700 kPa	T.C. 1400-2000 kPa
@max brake torque

NOTE: at max power, bmep is typically 10-15% less than the values above

Brake Specific Fuel	      250-300 g/kw-hr	200-250 g/kw-hr

Consumption, (bsfc)

Thermal Efficiency		20-35%		   25-45%

Combustion Efficiency		95-98%		   95-98%
                                             less for 2-strokes

Mechanical Efficiency	 90% mid-range		95% mid-range
				75% @max speed		85% @max speed

Volumetric Efficiency	   75-90% 4 stroke		85-95% 4 stroke

60-80% 2 stroke		70-95% 2 stroke
                                           over 100% if tuned

Abbreviations
H.P. = high performance	 N.A. = naturally aspirated	 T.C. = turbocharged