In-Cylinder Pressure Modeling

Names:

Orientation:

In this activity, you will contrast real and ideal Otto cycle engines from the standpoint of their pressure-volume, pressure-crankangle diagrams, and log pressure vs log volume behavior.  This will uncover a clever method for tracking in-cylinder heat release that applies to any engine cycle.

Learning Objectives:

- Enhance your intuition about real and ideal thermodynamic cycles by relating pressure-volume, pressure-crankangle, and log pressure vs log volume plots.

- Visualize in-cylinder heat release by analyzing log pressure versus log volume plots.

Targeted Skills:

Diagramming – clarifying relationships through visual representation

Reasoning with theory – explaining data with accepted knowledge

Sharing knowledge – effectively presenting relevant facts and interpretations

- Sketch an air-standard Otto cycle on a PV diagram.  Identify all processes, including ideal intake and exhaust. USE A SOLID LINE.  Overlay a PV diagram for a complex fuel-air cycle that includes effects of (a) finite combustion time,
(b) wall heat transfer, (c) finite valve opening/closing times, and (d) blowdown before BDC.  USE A DASHED LINE.

- On a separate graph, sketch a pressure-crankangle diagram over 720 degrees for a motored engine with no combustion.  Assign top dead center (TDC) at the beginning of the intake stroke to be -360 degrees.  This will make TDC at the end of compression to be 0 degrees.  USE A DOTTED LINE.  On this second graph, overlay a pressure-crankangle diagram for an air-standard Otto cycle.  Label the start and end of each process.  USE A SOLID LINE.  On this second graph, now overlay a pressure-crankangle diagram for a complex fuel-air cycle including the effects listed above.  USE A DASHED LINE.

- Represent compression, combustion, expansion, and heat rejection for this engine to a third graph which displays log pressure versus log volume.  Use a SOLID LINE for the air-standard cycle and a DASHED LINE for the complex fuel-air cycle.  Clearly identify each process.  What is the slope of the polytropes representing compression and expansion?

- On a fourth graph, sketch the mass burned fraction as a function of crankangle for an air-standard Otto cycle.  USE A SOLID LINE.  On this graph, overlay the mass burned fraction as a function of crankangle for a complex fuel-air cycle.  USE A DASHED LINE.  Clearly show the start and end of combustion.

- How do these graphs change when the mixture is leaned out?

- How do these graphs change as engine speed is increased?