HAAS Mill Setup Checklist

1. Program preparation

  - Ensure drawing package and dimensioning meet senior design criteria

  - Run simulation in MasterCAM and have code approved by a mentor

  - Have drawings and a machining plan on hand for quick access

2. Maintenance

  - Check coolant; make sure container is ¾ full

  - Clean chips from operating table and machinery

  - Make sure tools are sharp and in operating condition

3. Startup

  - Turn HAAS Mill on (green POWER ON button)

  - Sign and date sheet on right side of control interface

  - Perform warm-up if machine has not been run in 3 days

LIST PROG => Spindle warm-up => Start

4. Tool Preparation

  - Setup tools in tool holders on cart

  - Put tools in proper order on the HAAS carriage

  - Place material securely in the jig

  - Zero z-axis for each tool implementing feeler gauge

  - Zero x- and y-axis to common corner on the material to be machined

5. Program Loading

  - Upload the program

LIST PROG => select program using CURSOR => SELECT PROG

  - Perform a dry run